## Slide 1: WF on UE mandatory channel bandwidth
Nokia, …
3GPP TSG-RAN WG4 #84
Berlin, Germany, 21st – 25th August, 2017
R4-1708845

## Slide 2: Background
In RAN4 AH#2, WF on band specific UE channel bandwidth (R4-1706982) was greed but it was FFS how to choose the set of CBW to mandate UE to support.

## Slide 3: Background: LTE refarming bands
NR Band | Data SCS = 15kHz |  |  |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  | Data SCS = 60kHz (for more than 1GHz bands) |  |  |  |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz | 25MHz | [40MHz] | [50MHz] | 10MHz | 15MHz | 20MHz | 25MHz | [40MHz] | [50MHz] | [60MHz] | 10MHz (NOTE) | 15MHz | 20MHZ | 25MHz | [40MHz] | [50MHz] | [60MHz]
1.427-1.518G | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 1 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 3 | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes |  |  | 
Band 7 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  | 
Band 8 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | NA |  |  |  |  |  | 
Band 20 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 28 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 41 |  | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes | Yes | Yes |  | Yes | Yes | Yes
Band 66 | Yes | Yes | Yes | Yes |  | Yes |  | Yes | Yes | Yes |  | Yes |  |  | Yes | Yes | Yes |  | Yes |  | 
Band 70 | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes |  |  | 
Band 71 | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes |  |  |  |  | NA |  |  |  |  |  | 
NOTE: 90% spectrum utilization may not be achieved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Changes from R4-1706982
25MHz added to band 3 (R4-1707844)
Minimum bandwidth 10MHz for Band 41 (Draft chairman’s minutes after Monday)

## Slide 4: Background: NR bands
Sub6
mmW
NR Band | Data SCS = 60kHz |  |  | Data SCS = 120kHz |  |  | 
 | 50MHZ | 100MHz | [200MHz] | 50MHZ | 100MHz | [200MHz] | 400MHz
24.25-29.5 GHz | Yes | Yes | Yes | [Yes] | Yes | Yes | Yes
31.8-33.4GHz | Yes | Yes | Yes | Yes | Yes | Yes | Yes
37-40 GHz | Yes | Yes | Yes | Yes | Yes | Yes | Yes
NR Band | Data SCS = 15kHz |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  |  | Data SCS = 60kHz (for more than 1GHz bands) |  |  |  |  |  |  | 
 | 10MHZ | 15MHz | 20MHZ | 40MHz | 50MHz | 10MHZ | 15MHz | 20MHz | 40MHz | 50MHz | 60MHz | 80MHz | 100MHz | 10MHz (NOTE) | 15MHz | 20MHz | [40MHz] | 50MHz | 60MHz | 80MHz | 100MHz
3.3-4.2 GHz | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes
4.4-4.99 GHz |  |  |  | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes | Yes
NOTE: 90% spectrum utilization may not be achieved |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Changes from R4-1706982: Proposal 1 from R4-1708550 is agreed.

## Slide 5: Agreement
  UE maximum channel bandwidth is a UE capability.
    It is FFS if the UE capability is per band or a group of bands (such as sub6 and mmWave)
  UE shall meet either a single carrier or CA based RF requirements for the channel bandwidths in Slide #3-#4 that is equal to or smaller than UE maximum channel bandwidth for any SCS.
  RAN4 should agree some threshold value for which BW’s should be supported by single CC configuration.