## Slide 1: WF on Channel Raster for NR
Qualcomm Incorporated, Ericsson, Vodafone, AT&T, Sprint, Verizon, ZTE
3GPP TSG-RAN WG4 RAN4 #84
Berlin, Germany, 27th-29th, 2017
R4-1708850
Document for: Approval

## Slide 2: Agreements on channel raster
Channel raster for LTE re-farming bands up to 2.4GHz (frequency range below Band 41) is based on 100kHz(same as LTE)
  FFS: Potential optimization for of the placement of secondary carrier including RB-alignment between primary and secondary carrier
For Band 41, FFS 100kHz channel raster or subcarrier based raster should be used.
Channel raster for Bands above 2.6GHz (above Band 41) is tentatively agreed to be a subcarrier based raster (i.e 15kHz for range 1 and 60kHz for range 2), pending further check at AN4 NR AH#3 and RAN1 decision
  If subcarrier based raster is finally agreed, Eexact position of the subcarrier raster in each band to be agreed in RAN4 NR AH#3
Send LS to RAN1 to ask RAN1 to enable “floating sync” in RAN4#83 (see Annex), subject to feasibility
  Floating sync enables SCS based raster and down selection of the sync raster for bands using 100kHz raster

## Slide 3: Agreements on sync raster
Sync raster will be defined such that there is a minimum number of entries for each band
Sync raster entries will be included in the specifications for each band
Sync raster entries will be defined for initial system acquisition, sync blocks can be transmitted in other frequency locations if the position is signaled to the UE

## Slide 4: Annex – “Floating sync” description
Sync block is not RB aligned with the data RBs in the channel as shown in the Figure
  There is an arbitrary offset between the edge of the sync block RBs and the edge of the data RBs in the channel, this offset can be up to 11 REs
Enables multiple channels that are subcarrier grid aligned but not RB grid aligned to use the same sync block location
  Different channels that are offset by up to 11REs in frequency can re-use the same sync block frequency location
Description can be found in R4-1707335