## Slide 1: WF on Requirement for 55dBm EIRP Transportable Stations
Verizon, Ericsson, Qualcomm, Qorvo, Huawei, ZTE, Nokia
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany, 21 - 25 August, 2017
Agenda Item: 9.3.5
R4-1708853

## Slide 2: Background
Contribution on Requirement for 55dBm EIRP Transportable Stations has been discussed in RAN4#84:
  [1] R4-1707760 Requirement for 55dBm EIRP Transportable Stations Verizon UK Ltd

## Slide 3: Way forward on Simulation Assumptions [1]
Adopt the agreed simulation assumptions used by RAN4 for WP5D NR 30GHz and 45GHz UL coexistence simulation:
  [2] 3GPP TR 38.803 v14.0.0, “Study on New Radio Access Technology; RF and co-existence aspects”.
Except that:
  UE max TX power is [35 41dBm] at the antenna connector (i.e. 55dBm EIRP with [5 dBi] element gain, [10*log(32) = 15 6dBi] array gain and 3dBi polarization gain).
  CLx-ile = [106] + 10*log10(200/X) which represents high power transportable stations are aimed for UL coverage enhancement.
  Adopt BS noise figure values for ITU WP5D response (i.e. 10dB for 30GHz and 12 dB for 45GHz).

## Slide 4: Way forward on Simulation Assumptions [2]
Consider following other assumptions:
  Urban macro scenario in 30GHz with [ISD = 300m] and dense urban micro scenario in 30 GHz and 45GHz
  80% outdoor and 20% indoor users in all cases
  [1.5] meters of UE antenna elevation
  With directional antennas at both BS and UE, same as in 3GPP TR 38.803 v14.0.0
  Channel models will be the same as in 3GPP TR 38.803 v14.0.0
Consider whether to include 23dBm UE and 55dBm CPE in the same deployment for some of the requirements
Consider only UL simulations

## Slide 5: Way forward on Work Plan
Via email discussions by 2017/09/02
  Finalize the simulation assumptions including the antenna patterns at CPE, channel model, UL power control formula, etc
In RAN4 NR AH#3
  Interested companies are encouraged to provide coexistence simulation results.
In RAN4 #84bis
  Simulation results should be finalised
  Coexistence requirements, including ACLR and ACS requirements, should be finalized
  Interested companies are encouraged to provide simulation results on other requirements, e.g., blocking, etc.
    Interested companies are encouraged to provide investigations related to feasibility of achieving certain requirement levels which should be considered and taken to account.
In RAN4#85,
  Other requirements, e.g. Blocking, etc to be finalized
  All core requirements for high power transportable stations are specified.
    Interested companies are encouraged to provide investigations related to feasibility of achieving certain requirement levels which should be considered and taken to account.
  Work on requirements for 55dBm EIRP transportable stations does not have impact on completion of requirements for normal UEs in 28GHz band.