## Slide 1: WF on BS transmitter intermodulation for NR sub-6GHz
ZTE, []
3GPP TSG-RAN WG4-NR Meeting # 84
Berlin, Germany, 21 – 25 August, 2017
R4-1708871

## Slide 2: Agreements
In RAN4#84, BS transmitter intermodulation was discussed and the following proposal was agreed:
  Proposal : similar to LTE, for NR sub 6GHz, only “Co-location transmitter intermodulation” case should be defined for Range 1-C-N, and both “Co-location transmitter intermodulation” and “Intra-system transmitter intermodulation” cases for range 1-C-A.

## Slide 3: Way Forward
Co-location transmitter intermodulation case for conductive requirements:
  Use the same interfering signal by identifying the worst case regardless of Bands, SCS of wanted signal, CBW of wanted signal, BS class :
    interfering signal type:
      FFS: NR or LTE signal
    interfering signal channel bandwidth
      FFS
    interfering signal level:
      Rated total output power in the operating band – 30 dB

## Slide 4: Way forward (Cont’d)
Intra-system transmitter intermodulation case
  the way to define interfering signal in AAS could be reused for NR range 1-C-A.
    Specify NR signal of the same channel bandwidth as the wanted signal as interfering signal
    Power level declared by the base station manufacturer