## Slide 1: Way Forward on RRM with Network-Based CRS Interference Mitigation
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #84bis R4-1711304
Dubrovnik, Croatia, 9th – 13th October 2017

## Slide 2: General
NB-IoT
  CRS can be assumed in resource blocks where NRS are present, only in presence of inband NB-IoT UEs when inband-SamePCI is indicated
HF-FDD
  Full-bandwidth CRS shall be assumed during UL transmission gaps for HD-FDD UEs

## Slide 3: Additional details for CONNECTED Mode
RLM
  Full BW CRS is assumed for UE in bad radio channel conditions (e.g., based on RS-SINR, RSRQ, or CQI) in the serving cell
MPDCCH monitoring
  No full BW CRS is needed between MPDCCH monitoring occasions, if not receiving data
  Warm up TBS, cool down TBD
PRS subframes
  Full BW CRS during PRS subframes
  Warm up 0 ms, cool down 0 ms
RA due to HO
  Msg2/msg4: Full BW CRS from the start of RAR window until HO complete
SCell activation/deactivation of configured Scells
  Full BW CRS during SCell activation period and when the SCell is activated except for the SCell deactivation period
SR-over-PRACH
  Full BW CRS from the start of the RAR window until the contention resolution timer has been stopped
SR-over-PUCCH
  3 ms after the subframe in which the UE sent SR on PUCCH and until UL grant has been transmitted
  Note: Other scenarios are not precluded

## Slide 4: Additional Details for IDLE Mode
RA
  Msg2/4: full BW CRS from the start of RAR window until DRX configuration is applied
SI reading
  SIB1: warm up TBD, cool down TBD
  SI windows: full BW is needed from the start of SI-window until the last SI message repetition within the window, warm up TBD, cool down TBD
eDRX
  Outside PTW: no additional warm up before and no cool down after PTW (within PTW, there will warm up periods for DRX, PO, etc.)
Note: Other scenarios are not precluded