## Slide 1: WF on Evaluation of IQ Leakage for V2X Multi Carriers Operation
Qualcomm Inc.
R4-1711592
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, 9 – 13 Oct, 2017

## Slide 2: Background
  For intraband CA IBE requirement: there is an IQ leakage allowance of 25dBc.
  This can cause near far effect for V2X
20-30 dBc Link Difference

## Slide 3: Way Forward
RAN4 to conduct System Simulation to evaluate this effect.
Simulation Assumption following that in Annex A of TR36.885 unless otherwise stated in this WF.
Link level simulation mapping model is refered in Annex A in TR36.785
Consider urban and freeway scenarios
UE speed:
  60 km/h for urban.
  140 km/h for freeway.
Number of UEs: Inter UE distance 2.5sec times UE speed.
AWGN channel.

## Slide 4: Coexistence Scenarios
Simulate 1CC and 2CCs of 10 MHz
  Option 1:
    Number of UE for 1 CC following inter UE distance.
    Double the number of UEs for 2CCs case.
  Option 2:
    Number of UE for 2 CC following inter UE distance.
    Half the number of UEs for 2CCs case.
IQ Rejection is 30dBc (IQR)
IQ leakage is 25 + X dB with X >= 0 and X <=5. (IQL)
IQ interference (IQI) = 1 / (1/IQR + 1/IQL).
IQ regions are symmetrical wrt to agregated Channels center.

## Slide 5: Coexistence Criteria
Range reduction at 90 % PRR is less than 10%.
If criteria does not meet for IQL = 30dBc, then IQL is chosen as 30dBc.
The timeline for this work is 3 meetings.
The simulated IQL is typical IQL.
Minimum requirement is min(25dBc, IQL – 3dB offset)