## Slide 1: Africa Band Key points about 3300-3400MHz band
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting 84Bis
Dubrovnik , Croatia, 09th – 13th October, 2017
R4-1711612
Agenda Item: 8.12.1
Document for: Approval

## Slide 2: Background
At the 3GPP TSG RAN Meeting #76 in West Palm Beach, USA June 5 - 8, 2017, a new WI about the study of the TDD in the C-band (3300-3400 MHz) has been approved.
To evaluate the need to take into account directly in the standard the current regulation, in this contribution, several regulatory information are provided.
In the followed slides, several key points, e.g. Power, sensitivity … are proposed for approval

## Slide 3: Need to take into account in the standard the regulation?
ATU response to the 3GPP LS (R4-1709188)
The Doc R4-1710124, ATU response to 3GPP RAN4:
In conclusion, ATU is of the view that it is not necessary to introduce further requirements in the 3GPP specification of the new band to protect incumbent radar services.
Also, the contribution R4-1708452 (Huawei, Hisilicon) as study the need (or not) to take into account some specific regulations in the 3GPP standard.
The conclusion is that the 3GPP standard does not need to take into account any specific regulation to protect incumbent users.

## Slide 4: Proposals for approval 1/3
Proposal 1: Numbering band => B52
Proposal 2: E-UTRA channel numbers =>
  59140 to 60139
  Frequency start: 3300MHz
Proposal 3: Not take into account any specific technical continuation to take into account the regulation framer (in band & adjacent band) in the 3GPP standard,
  UE => No A-MPR
  BS => No additional filter
E-UTRA Operating Band | Downlink |  |  | Uplink |  | 
 | FDL_low [MHz] | NOffs-DL | Range of NDL | FUL_low [MHz] | NOffs-UL | Range of NUL
52 | 3300 | 59140 | 59140–60139 | 3300 | 59140 | 59140–60139
Table X-2: EARFCN allocated for E-UTRA Band 52
E‑UTRA Operating Band | Uplink (UL) operating band BS receive UE transmit |  |  | Downlink (DL) operating band BS transmit UE receive |  |  | Duplex Mode
 | FUL_low – FUL_high |  |  | FDL_low – FDL_high |  |  | 
52 | 3300 MHz | – | 3400 MHz | 3300 MHz | – | 3400 MHz | TDD
Table X-1 E-UTRA frequency bands

## Slide 5: Proposals for approval 2/3
Proposal 4: UE reference sensitivity power level
  Taking into account that B52 and B42 have very similar technical characteristics, it is proposed to apply to the B52 the same UE reference sensitivity than the B42.
  Thus, for B52 the reference sensitivity is specified in Table below for general case:
  For specific case, UE(s) equipped with 4 antenna ports, the following additional requirements described in the table below is applied for B52:
Proposal 5: BS & UE power emission
  Same as B42
Channel bandwidth |  |  |  |  |  |  | 
E-UTRA Band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex Mode
52 |  |  | -99 | -96 | -94.2 | -93 | TDD
Reference sensitivity QPSK PREFSENS
Channel bandwidth |  |  |  |  |  |  | 
E-UTRA Band | 1.4 MHz (dBm) | 3 MHz (dBm) | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | Duplex Mode
52 |  |  | -101.2 | -98.2 | -96.4 | -95.2 | TDD
Reference sensitivity QPSK PREFSENS

## Slide 6: Proposals for approval 3/3
Proposal 6: Spurious emissions and UE coexistence
  Same technical parameters as B42. But, for only the specific the technical constraints NS_22 & NS_23, it is proposed 2 options as described just below,
  In the case of un-synchronized TDD networks, for the B42 there are some additional technical constraints which are NS_22 and NS_23. At the 3GPP TSG-RAN WG4 Meeting 84Bis in Dubrovnik , Croatia, 09th – 13th October, 2017, 2 options has been proposed:
    Option 1 => To take into account the case of unsynchronized TDD networks and taking into account that B52 and B42 have very similar technical characteristics, it is proposed to apply to the B52 the similar technical constraints than NS_22 and NS_23,
    Option 2 => It is assuming that the TDD networks will be synchronized because this is the best option to avoid interferences and guard bands, thus it is proposed to NOT apply to the B52 the similar technical constraints than NS_22 and NS_23.
  During the next meeting RAN4#85 (2017-11-27 - Reno, Nevada(US)), it is decided to make a choice between the both options.
Proposal 7: Provide all relevant draft CRs for the next 3GPP RAN4 meeting