## Slide 1: 3GPP TSG-RAN WG4 Meeting 84bis Dubrovnik, Croatia, 09-14 October 2017
Ericsson, MediaTek
WF on synchronous and asynchronous definitions for LTE-NR DC in Rel-15
R4-1711964

## Slide 2: Background
Following contributions in RAN4 discuss the issue:
  R4-1710210, Consideration on synchronization requirements for LTE NR DC, Huawei, HiSilicon [RAN4#84bis]
  R4-1710891, Synchronization requirements for TDD intra-band LTE-NR DC, MediaTek [RAN4#84bis]
  R4-1711478, Definition of synchronous and asynchronous Dual connectivity in Rel-15 LTE-NR combinations, Ericsson [RAN4#84bis]
  R4-1710616, Discussion on MRTD and MTTD in Dual Connectivity, LG [RAN4#84bis]
  R4-1707699, LTE-NR DC power sharing assumptions below 6GHz, InterDigital [RAN4#84]

## Slide 3: Scope
This WF includes:
  Inter-band LTE NR DC
  Intra-band LTE-NR DC
All duplex combinations are included:
  TDD-TDD (PCell-PSCell)
  FDD-FDD (PCell-PSCell)
  TDD-FDD (PCell-PSCell or PSCell-PCell)
LTE CC will be in FR1 while NR CC can be either FR1 or FR2.

## Slide 4: Inter-band LTE-NR DC (1/2)
All UEs support asynchronous DC between LTE and NR for inter-band LTE-NR in Rel-15.
  Asynchronous here refers to subframe/slot timing boundary alignment
Following MRTD and MTTD is defined:
LTE PCell SCS (kHz) | NR PSCell SCS (kHz) | MRTD (µs) for asynchronous operation | MTTD (µs) for asynchronous operation
15 | 15 | 500 | 500
15 | 30 | 250 | 250
15 | 60 | 125 | 125
15 | 120 | 62.5 | 62.5

## Slide 5: Inter-band LTE-NR DC (2/2)
For inter-band TDD-TDD (PCell-PSCell) and inter-band TDD-FDD (PCell-PSCell or PSCell-PCell) combinations,
  Simultaneous RXTX in DC operation can be supported based on UE Capability.

## Slide 6: Intra-band LTE-NR DC (1)
For TDD-TDD case,
  Synchronous DC operation as well as NR DL/UL resource assignment to avoid DL/UL interference with LTE TDD is needed for intra-band LTE-NR DC.
  It is proposed to only consider collocation scenario for intra-band LTE-NR DC in Rel-15.
  UE shall support the synchronous TDD-TDD LTE-NR intra-band DC provided that the MRTD at the UE does not exceed values shown in the table below:
LTE SCS (kHz) | NR SCS (kHz) | MRTD (µs) for synchronous operation | MTTD (µs) for asynchronous operation
15 | 15 | TBD | NA
15 | 30 | TBD | NA
15 | 60 | TBD | NA

## Slide 7: Intra-band LTE-NR DC (2)
For FDD-FDD intra-band LTE-NR,
  It is proposed to only consider collocation scenario for intra-band LTE-NR DC in Rel-15.
  If UE supports asynchronous dual connectivity assuming separate RF chains, following MRTD and MTTD is defined in this case:
LTE PCell SCS (kHz) | NR PSCell SCS (kHz) | MRTD (µs) for asynchronous operation | MTTD (µs) for asynchronous operation
15 | 15 | 500 | 500
15 | 30 | 250 | 250
15 | 60 | 125 | 125