## Slide 1: On band n5 usage in Japan
NTT DOCOMO, INC.
Agenda Item : 9.2.1 R4-1713182 Document for : Approval
GPP TSG-RAN WG4 Meeting #85
Reno, US, 27th November – 1st December 2017

## Slide 2: Introduction
Summary of proposal
  This material proposes to make n5 usage in Japan possible and provide specific requirements to make it.
Motivation
  Now most of the LTE Band 19 capable terminals support LTE Band 5 as well since the frequency range of LTE Band 5 completely cover that of LTE Band 19 so that they can use common analogue components.
  Despite that fact that the common analogue devices are used for both bands, they have been defined in different ways. This leads to more tests to make devices have capabilities for two similar bands and more band combinations. This also loses opportunities of international roaming.
    Note that LTE Band 5 is not only available in US but also in some other countries.
  Hence, we believe it is time to make n5 available in Japan as 850 MHz band.
B19(Uplink)
B19(Downlink)
875
890
845
830
B5(Uplink)
B5(Downlink)
894
824
849
869
B18(Uplink)
B18(Downlink)
815
860
B18 (KDDI)
B19 (DOCOMO)
B5

## Slide 3: Overview on things to make n5 available in Japan
Fundamental reason why LTE B5 has not been available in Japan
  The fundamental difference is that LTE B5 does not deal with 15 MHz channel bandwidth while LTE B19 has to does.
    Note that making up to 10MHz channel bandwidths available in Japan could be possible if we introduce resource block restriction method to protect LTE B18 and B19 DL without NS signaling and the associated A-MPR.
For NR case,
  Now n5 would be able to cover necessary channel bandwidths such that 5, 10 and 15 MHz [1]
  In principle, the only thing to make n5 available in Japan is to introduce requirements to protect 860-890 MHz (DL of LTE B18 and LTE B19) with -40 dBm/MHz and associated NS and A-MPR requirements.
  Note that from UE co-existence perspective, basically LTE B5 already covers what is needed for operation in Japan as can be seen in the spurious emission UE co-existence table in Table 6.6.3.2-1 TS36.101.
  Note that the existing LTE Band 5 operators do NOT have to pay attention to Japan specific signaling when they operate n5. This is because the NS signaling does not have to be signaled to UEs in their network.
[1] R4-1712165, Dish Network, NTT DOCOMO, Required UE single CC CH BW support in NR, Nov. 2017.

## Slide 4: Things to make n5 available in Japan
n5 needs to support the equivalent requirements related with NS_08 specified in 6.6.3.3.3 and Table 6.2.4-1 in 6.2.4 in TS 36.101.
  Extract of Table 6.2.4-1 in TS 36.101
  Extract of Table 6.6.3.3.3-1 in 6.6.3.3.3 in TS 36.101
Note:
  In principle, the above requirements would not impact on n5 capable analogue device implementation due to the following reasons.
    Currently LTE B19 terminals use the same analogue components as those of LTE B5 and the required A-MPR for LTE B19 can be satisfied since the A-MPR requirement was generated based on LTE band 5 components such as duplexer.
    The same applies to n5 as far as the required A-MPR is generated based on currently available LTE band 5 analogue components.
Network Signalling value | Requirements (subclause) | E-UTRA Band | Channel bandwidth (MHz) | Resources Blocks (NRB) | A-MPR (dB)
NS_08 | 6.6.3.3.3 | 19 | 10, 15 | > 44 | ≤ 3
Frequency band (MHz) | Channel bandwidth / Spectrum emission limit (dBm) |  |  | Measurement bandwidth
 | 5MHz | 10MHz | 15MHz | 
860 ≤ f ≤ 890 | -40 | -40 | -40 | 1 MHz

## Slide 5: Conclusion
Observation:
  n5 will become available in Japan by introducing requirements equivalent to NS_08 specified in 6.6.3.3.3 and Table 6.2.4-1 in 6.2.4 in TS 36.101.
    Note that minor changes for spurious emission UE co-existence are needed.
  This does not cause trouble to n5 UE implementation specifically analogue components as far as the A-MPR is generated based on currently available LTE B5 duplexers.
  The existing operators do not have to pay attention to Japan specific signaling.
Proposal:
  Introduce requirement equivalent to NS_08 specified in 6.6.3.3.3 and Table 6.2.4-1 in 6.2.4 in TS 36.101 into TS 38.101-1 to make the band n5 available in Japan.