## Slide 1: Way forward on euCA RRM requirements
3GPP TSG-RAN WG4 #86 R4-1803104
Athens, Greece, February 26nd - March 2nd, 2018
Agenda item: 6.25
Nokia, Nokia Shanghai Bell

## Slide 2: Background
During the meeting RAN4 had discussions based on the summary document R4-1803077 Summary of contributions for enhancing CA utilization.
3 topics were discussed based on the company input:
  New SCell state.
  Measurements for fast CA setup.
  Direct SCell activation.

## Slide 3: Fast Scell activation agreements
Related to transitions delays following was agreed:
  fast cell activation -> activated: n+8 (FDD non-MBSFN, others are FFS)
  activated –> fast SCell activation: n+8
  fast cell activation state -> deactivated state: n+8
  Whether the above agreements are applicable to uplink CA case is FFS.
Related to interrupts at state transitions following was agreed:
  Interrupt for transition between fast SCell state and deactivated state: re-use existing active -> deactivated requirements.
  For the transition between the fast Scell state and the activated state, there could be interruption.

## Slide 4: Open aspects for further discussions
Fast Scell activation
  missing transition delays from deactivation to fast activation due lack of RAN2 agreement on introducing this state transition.
    If introduced RAN4 will introduce transition delay
  In fast SCell state there may be some interruption on the CQI reporting. More investigation is needed for the concrete number for the interruption in the future meeting.
  Regarding measurement for new Scell state RAN4 need to discuss:
    RRM measurement requirements in new Scell state (core).
    CQI measurements accuracy (performance).

## Slide 5: Open aspects for further discussions
Measurements for fast CA setup
  Measurement Requirements
    Minimum number of extra inter-frequency candidate layers to be measured for reporting
    Introduction of measurement time limitation
  Measurement accuracy
    It seems measurement accuracy can be introduced (not agreed)
    Measurement accuracy of reported cells.
  Side conditions
    Known cell condition
  Any impact on existing idle mode RRM requirement

## Slide 6: Open aspects for further discussions
Direct SCell activation
  Which point defines the beginning of the SCell activation
  Activation delay length
  Interruptions