## Slide 1: Way forward on PSCell addition delay and SCell activation delay
CATT
3GPP TSG-RAN WG4 #86 Athens, Greece, Feb 26th- Mar 2nd, 2018
R4-1803482

## Slide 2: Background
SCell activation delay
  It was agreed in RAN4 Adhoc#1801 that SCell activation delay requirements (Tactivation_time) is consisted of :
    RF warm up excluding AGC settling: TBD and independent of SCS
    AGC settling: N1 SMTC periods for known and N2 SMTC periods for unknown cells
    PSS/SSS and SSB index acquiring:
      X1 SMTC periods for known cell
      X2 SMTC period for unknown cell
      X1 and X2 will be decided by RAN4#86
  Side condition: SINR ≥ -3dB
  Activation time for activation of multiple SCells; No. of SCells is FFS
PSCell activation delay
  It was agreed in RAN4 Adhoc#1801 that PSCell addition delay requirements was defined as:
Tconfig_PSCell = TRRC_delay + Tactivation_time + TSFN_acquisition + TPCell_ DU + TPSCell_ DU
  Tactivation_time should be the same as defined in SCell activation delay

## Slide 3: PScell addition delay
TPCell_ DU is not needed anymore in NR PSCell addition delay
TSFN_acquisition in the PSCell addition delay equation is not needed, since it has already been covered by Tactivation
PSCell addition delay requirements can be defined as:
Tconfig_PSCell = TRRC_delay + Tactivation_time + TPSCell_ DU

## Slide 4: SCell Known condition
In SSB based SCell activation requirements, SCell in FR1 can be considered as known without MIB reading, known with MIB reading and unknown by considering the following conditions:
  During the period equal to max([5] measCycleSCell, [5] DRX cycles) for FR1 before the reception of the SCell activation command:
    the UE has sent a valid measurement report
    the SCell being activated is indicated as a synchronous cell or the UE has already decoded MIB of the target SCell
    the SCell being activated remains detectable according to the cell identification conditions specified in section [TBD],
  SCell being activated also remains detectable during the SCell activation delay according to the cell identification conditions specified in section [TBD].
  How to define the conditions for SCell known without MIB reading and SCell known with MIB reading is FFS

## Slide 5: SCell activation delay
Activation delay requirement will be different for case whether UE has to decode PBCH
Further study SSB based activation delay requirement Tactivation_time
  Tactivation_time is consisted of
    RF warm up excluding AGC settling: TBD and independent of SCS
    AGC settling: N1(*) SMTC periods for known and N2 SMTC periods for unknown cells
    PSS/SSS and SSB index acquiring:
      X1 SMTC periods for known cell provided that PSS/SSS detection and MIB reading are not needed
      X2 SMTC period for known cell provided that MIB reading is needed
      X3 SMTC period for unknown cell provided that PSS/SSS detection and MIB reading are needed
      X1, X2 and X3 will be decided by RAN4#86bis
RAN4 to study the improvement on Tactivation_time delay if network configure additional reference signals e.g. periodic TRS or aperiodic TRS
(*) Different N1 values depending on quality of gain state information is to be investigated.