## Slide 1: WF on UE measurement mode with MG for SA mode
Intel
3GPP TSG-RAN WG4 RAN#86bis
Melbourne, Australia, Apr 16th- Apr 20th, 2018
R4-1804201
Document for: Approval

## Slide 2: Background
In this RAN4 meeting, LS (R4-1804202) was approved, in which we agreed the assumptions for UE measurement mode discussion for SA mode
In order to determine the UE measurement mode with measurement gap for SA mode, RAN4 would assume that,
In NR standalone mode,
(1) NR serving cell can configure both an FR1 gap pattern and an FR2 gap pattern to be active at the same time.
(2) If NR serving cell configures measurement gap for a UE, NR serving cell can also indicate if configured measurement gap applies to FR1/FR2 serving cell(s) (i.e. per UE gap) or applies to FR1 serving cell(s) (i.e. per FR gap to FR1) or applies to FR2 serving cell(s) (i.e. per FR gap to FR2).
RAN4 will continue work with the above assumptions and suggest RAN2 to design the corresponding signalings according to the above assumptions, unless RAN2 has any issue from the signaling perspective.

## Slide 3: WF on UE measurement mode with MG for SA mode
In current stage, the cases to analysed in RAN4 concentrate on the following scenarios:
Scenario 1: Serving cell is FR1 cell only, or Serving cells are NR CA in FR1
Scenario 2: Serving cell is FR2 cell only, or Serving cells are NR CA in FR2
Scenario 3: Serving cells are FR1+ FR2 CA
For UE who supports per-UE gap only, only per-UE gap can be configured to this UE.
For UE who supports per-FR gap, the UE measurement mode summary is as next slide.

## Slide 4: WF on UE measurement mode with MG for SA mode
 | Measurement object involves LTE, FR1 only | Measurement object involves LTE, FR1 and FR2 | Measurement object involves FR2 only
Serving cell configure per-UE gap | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement
Serving cell configure per-FR gap for LTE/FR1 only | FFS | FFS | FFS
Serving cell configure per-FR gap for FR2 only | FFS | FFS | FFS
Serving cell configure per-FR gaps for LTE/FR1 and FR2 | FFS | FFS | FFS
Companies are encouraged to provide the analysis for the “FFS” in the above table for scenario 1, 2 and 3.