## Slide 1: WF on NR CA, EN-DC and NR DC notation
Sprint, Nokia, Dish
3GPP TSG-RAN WG4 Meeting #86bis R4-1805661 Melbourne, AU, 16th – 20th April, 2018

## Slide 2: Background
Proposals for notation in R4-1804223 [1], R4-1804029 [2], R4-1803750 [3]

## Slide 3: Is Max BW needed?
Some proposals included maximum aggregated BW numbers in the notation, like CA_nX(D,250)
This leaves open the issue of the tables possible getting larger and larger as additional BWs are supported
The Maximum BW can be implied by #CCs Band X * Max BW X + #CCs Band Y * Max BW Band Y
For this reason, max BW is not needed in the notation

## Slide 4: Way Forward Proposal 1 BW Classes
Contiguous EN-DC bandwidth class | Number of contiguous CC | 
 | LTE | NR
AA | 1 | 1
B | 1 | 1
CA | 2 | 1
AC | 1 | 2
JK | J | K
Table 1: Contiguous EN-DC bandwidth classes

## Slide 5: Way Forward Proposal 2 NR CA BW Class Notation
Type |  | Notation | Note
NR CA | Intraband contiguous | CA_nXC | Already used and follows LTE
 | Intraband non-contiguous example 1 | CA_nX(8A) | new way compared to LTE notation which would be CA_n257A-n257A-n257A-n257A-n257A-n257A-n257A-n257A using band n257 as an example
 | Intraband non-contiguous example 2 | CA_nX(3A-C) | new way compared to LTE notation which would be CA_n257A-n257A-n257A-n257C using band n257 as an example
 | Interband CA | CA_nXA-nYA | Already used and follows LTE

## Slide 6: Way Forward Proposal 3 EN-DC BW Class Notation
Type |  | Notation | Note
EN-DC | Intraband contiguous | DC_(n)XAA | 1 LTE, 1 NR, max BW ≤ max LTE BW + max NR BW
 |  | DC_(n)XB | Already used 1 LTE, 1 NR, max BW ≤ 20 MHz
 |  | DC_(n)XJK | J LTE, K NR
 | Intraband non-contiguous | DC_XA_nXA | Non-contiguous EN-DC with 2 sub-blocks
 |  | DC_XC_nXC | Non-contiguous EN-DC with 2 contiguous LTE sub blocks and 2 contiguous NR sub-blocks
 |  | DC_XA-XA_nX(3A) | Non-contiguous EN-DC with 2 non-contiguous LTE sub blocks and 3 non-contiguous NR sub-blocks
 | Interband | DC_XA_nYA | Follows LTE
Note: LTE CA and NR CA BW classes are used in EN-DC

## Slide 7: Way Forward Proposal 4 NRDC BW Class Notation
Type |  | Notation | Note
NR DC | Interband CA | DC_nXA-nYA | Follows LTE

## Slide 8: References
[1] R4-1804223 Proposal for NR CA, EN-DC and NR DC Notation, SPRINT
[2] R4-1804029 Notation for NR non-contiguous intraband CA, Nokia, Nokia Shanghai Bell
[3] R4-1803750 Considerations on NR CA & EN DC notation, ZTE Corporation