## Slide 1: Way forward on Scell activation delay
Intel, [], …
R4-1806267
3GPP TSG-RAN WG4 Meeting #87 Busan, KR, 21th – 25th May, 2018
Agenda Item: 7.10.10.4

## Slide 2: SCell activation delay
Background: it was agreed in RAN4#86b that
  SSB based activation delay requirement Tactivation_time in FR1: Tactivation_time is consisted of
    MAC-CE message decode time
    RF warm up excluding AGC settling: TBD
    AGC settling: N1 SMTC periods for known and N2 SMTC periods for unknown cells
      The exact value of N1 and N2 are TBD
      It is FFS that the parameter value of N1 shall depend on the SCell measurement cycle in use prior to the SCell activation
    PSS/SSS and SSB index acquiring:
      [2] SMTC periods for known cell provided that PSS/SSS detection and PBCH decoding are not needed
      [4] SMTC period for known cell provided that PBCH decoding is needed
      [5] SMTC period for unknown cell provided that PSS/SSS detection and PBCH decoding are needed
  SSB based activation delay requirement Tactivation_time in FR2: Tactivation_time is consisted of
    MAC-CE message decode time
    RF warm up excluding AGC settling: TBD
    AGC settling: N3 SMTC periods for known and N4 SMTC periods for unknown cells
      The exact value of N3 and N4 are TBD
      It is FFS that the parameter value of N3 shall depend on the SCell measurement cycle in use prior to the SCell activation
    PSS/SSS and SSB index acquiring:
      Rx beam sweeping should be considered for PSS/SSS detection and measurement for FR2 for both known and unknown cell
      The corresponding delay is FFS

## Slide 3: Proposal
Tactivation_time = Tmac_processing +Trf1 +Tssb +Tagc | SCell unknown | SCell known with MIB reading | SCell known
FR1 | [(K1+0.5.ms)+ 0.5ms + [5]*SMTC_period+ [2]*SMTC_period | [(K1+0.5.ms)+ 0.5ms + [4]*SMTC_period+ [2]*SMTC_period | [(K1+0.5.ms)+ 0.5ms + [2]*SMTC_period+ [2]*SMTC_period
FR2 | [(K1+0.5.ms)+ 0.5ms + [5*N]*SMTC_period+ [2*N]*SMTC_period | [(K1+0.5.ms)+ 0.5ms + [4*N]*SMTC_period+ [2*N]*SMTC_period | [(K1+0.5.ms)+ 0.5ms + [2*N]*SMTC_period+ [2*N]*SMTC_period
Proposal 1: Tactivation_time which is consisted of
    MAC
    RF warm up excluding AGC settling: TBD and independent of SCS
    AGC settling
    PSS/SSS and SSB index acquiring:
can be specified as:
It is noted that N can be less than the maximum RX beams numbers, e.g. N=[8].