## Slide 1: WF on UE measurement mode with MG for SA mode
Intel
3GPP TSG-RAN WG4 RAN#86bis
Melbourne, Australia, Apr 16th- Apr 20th, 2018
R4-1806334
Document for: Approval

## Slide 2: Background
In last RAN4 meeting, LS (R4-1804202) was approved, in which we agreed the assumptions for UE measurement mode discussion for SA mode
In NR standalone mode,
(1) NR serving cell can configure both an FR1 gap pattern and an FR2 gap pattern to be active at the same time.
If NR serving cell configures measurement gap for a UE, NR serving cell can also indicate if configured measurement gap applies to FR1/FR2 serving cell(s) (i.e. per UE gap) or applies to FR1 serving cell(s) (i.e. per FR gap to FR1) or applies to FR2 serving cell(s) (i.e. per FR gap to FR2).
In current stage, the cases to analysed in RAN4 concentrate on the following scenarios:
Scenario 1: Serving cell is FR1 cell only, or Serving cells are NR CA in FR1
Scenario 2: Serving cell is FR2 cell only, or Serving cells are NR CA in FR2
Scenario 3: Serving cells are FR1+ FR2 CA

## Slide 3: WF on UE measurement mode with MG for SA mode
Scenario 1: Serving cell is FR1 cell only, or Serving cells are NR CA in FR1 (UE support per-FR gap)
 | Measurement object involves LTE, FR1 only | Measurement object involves LTE, FR1 and FR2 | Measurement object involves FR2 only
Serving cell configure per-UE gap | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement
Serving cell configure per-FR gap for LTE/FR1 only | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR1 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR1 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement - UE fulfils the per-FR requirements for FR2 measurement objects based on effective MGRP=20ms | From scheduling opportunity and gap applicability perspective, - Invalid gap configuration (because no FR1 MO was configured) From measurement requirement perspective, - UE fulfils the per-FR requirements for FR2 measurement objects based on effective MGRP=20ms
Serving cell configure per-FR gap for FR2 only | Invalid gap configuration (no FR2 serving cell) | Invalid gap configuration (no FR2 serving cell) | Invalid gap configuration (no FR2 serving cell)
Serving cell configure per-FR gaps for LTE/FR1 and FR2 | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR1 applies to FR1 serving cell(s) - Invalid gap configuration for per-FR gap for FR2 (no FR2 serving cell and FR2 MO) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR1 applies to FR1 serving cell(s) - Invalid gap configuration for per-FR gap for FR2 (no FR2 serving cell) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement - Invalid gap configuration for per-FR gap for FR2, and UE behavior is unpredictable on FR2 | Invalid configuration (no FR2 serving cell and no FR1 MO)

## Slide 4: WF on UE measurement mode with MG for SA mode
Scenario 2: Serving cell is FR2 cell only, or Serving cells are NR CA in FR2 (UE support per-FR gap)
 | Measurement object involves LTE, FR1 only | Measurement object involves LTE, FR1 and FR2 | Measurement object involves FR2 only
Serving cell configure per-UE gap | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement
Serving cell configure per-FR gap for LTE/FR1 only | Invalid gap configuration (no FR1 serving cell) | Invalid gap configuration (no FR1 serving cell) | Invalid gap configuration (no FR1 serving cell)
Serving cell configure per-FR gap for FR2 only | From scheduling opportunity and gap applicability perspective, - Invalid gap configuration (because no FR2 MO was configured) From measurement requirement perspective, - UE fulfils the per-FR requirements for FR1 measurement objects based on effective MGRP=40ms | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR2 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR2 measurement - UE fulfils the per-FR requirements for FR1 measurement objects based on effective MGRP=40ms | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR2 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for FR2 measurement
Serving cell configure per-FR gaps for LTE/FR1 and FR2 | Invalid configuration (no FR1 serving cell and no FR2 MO) | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR2 applies to FR2 serving cell(s) - Invalid gap configuration for per-FR gap for FR1 (no FR1 serving cell) From measurement requirement perspective, - UE applies per-FR gap for FR2 measurement - Invalid gap configuration for per-FR gap for FR1, and UE behavior is unpredictable on FR1 | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR2 applies to FR2 serving cell(s) - Invalid gap configuration for per-FR gap for FR1 (no FR1 serving cell and FR1 MO) From measurement requirement perspective, - UE applies per-FR gap for FR2 measurement

## Slide 5: WF on UE measurement mode with MG for SA mode
Scenario 3: Serving cells are FR1+ FR2 CA (UE support per-FR gap)
 | Measurement object involves LTE, FR1 only | Measurement object involves LTE, FR1 and FR2 | Measurement object involves FR2 only
Serving cell configure per-UE gap | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement | From scheduling opportunity and gap applicability perspective, - it’s per-UE gap From measurement requirement perspective, - UE applies per-UE gap for measurement
Serving cell configure per-FR gap for LTE/FR1 only | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR1 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR1 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement - UE cannot perform measurement toward measurement objects in FR2 | Invalid gap configuration (FR1 gap cannot be used for FR2 MO)
Serving cell configure per-FR gap for FR2 only | Invalid gap configuration (FR2 gap cannot be used for LTE/FR1 MO) | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR2 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for FR2 measurement - UE cannot perform measurement toward measurement objects in LTE/FR1 | From scheduling opportunity and gap applicability perspective, - it’s per-FR gap to FR2 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for FR2 measurement
Serving cell configure per-FR gaps for LTE/FR1 and FR2 | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR1 applies to FR1 serving cell(s) - Invalid gap configuration for per-FR gap for FR2 (because no FR2 MO was configured) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement - Invalid gap configuration for per-FR gap for FR2, and UE behavior is unpredictable on FR2 | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR1 applies to FR1 serving cell(s) - per-FR gap for FR2 applies to FR2 serving cell(s) From measurement requirement perspective, - UE applies per-FR gap for LTE/FR1 measurement - UE applies FR2 gap for FR2 measurement; | From scheduling opportunity and gap applicability perspective, - per-FR gap for FR2 applies to FR2 serving cell(s) - Invalid gap configuration for per-FR gap for FR1 (because no FR1 MO was configured) From measurement requirement perspective, - UE applies per-FR gap for FR2 measurement - Invalid gap configuration for per-FR gap for FR1, and UE behavior is unpredictable on FR1