## Slide 1: Approach for finalizing simultaneous Rx/Tx discussion
NTT DOCOMO, INC.
R4-1807135
3GPP TSG-RAN4 Meeting #87
Busan, KR, 21th - 25th May, 2018

## Slide 2: Topics to be treaed
Harmonics and inter-modulation
Handling of higher configuration
schedule

## Slide 3: Harmonics and inter-modulation
If a certain configuration with harmonics and/or IMD should impact on the decision on if that configuration is Rx/Tx simultaneous capability or not?
Answer would be NO.
  Since harmonics and intermodulation do not always make that configuration infeasible.
  Example 1: DC_3A-n78A: 2nd harmonic
    2nd harmonic of Band 3 always hits somewhere within n78A.
    It does not mean this does always impact on real operation since some operators may have spectrum holding combination not impacted by the 2nd harmonic.
    In addition, LTE Band 3 and n78 can have sufficient isolation to use simultaneous RxTx operation in case the 2nd harmonic is not harmful.
  Example 2: DC_3A-n78A: IMD2
    IMD2 of dual uplink of 3A and n78 may hit somewhere within Band 3.
    It does not mean this does always impact on real operation since some operators may have spectrum holding combination not impacted by the IMD2 and also it depends on RB length and positions in each band. Note in case the IMD2 does not fall into the being operated Band 3, dual uplink must be able to used. Without simultaneous Rx/Tx capability, even single UL switched is not possible or meaningless.

## Slide 4: Example handling of higher order configuraiton(1/2)
Case 1: all the fallback modes are simultaneous Rx/Tx mandatory.
  Example 1: DC_1A-2A-3A-4A-n78
    Provided that 1A-n78, 2A-n78, 3A-n78 and 4A-n78 are all simultaneous Rx/Tx are mandatory and in CA_1A-2A-3A-4A, any band can be Pcell, then, the DC_1A-2A-3A-4A_n78 is simultaneous Rx/Tx is mandatory with all paired UL configurations.
Case 2: One LTE or NR band cannot be Pcell.
  NR CA without Dual band uplink with different bands
    Example 2: CA_n1A-n41A
      Currently in LTE, DL_1A-41A_UL_1A is allowed while DL_1A-41A_UL_41 is not allowed. Note that the latter is being discussed so that the status may change.
      Thus, simultaneous Rx/Tx is possible for the former while it is not for the latter.
  NR CA with Dual band uplink with different bands
    Example 3: CA_n1A-n8A-n41A_UL_n1A-n41A or n1A-n8A or n8A-n41A
      Only CA_n1A-n8A-n41A_UL_n1A-n8A is possible to be simultaneous Rx/Tx in case CA_n1A-n41A_UL_n1A-n41A is not still allowed.

## Slide 5: Example handling of higher order configuraiton(2/2)
DC case with Dual uplink with different bands
    Example 1: DC_1A-3A-8A-n41A_UL_1A_n41A or 3A_n41A or 8A_n41A
      EN-DC of DC_1A-3A-8A_n41A is NOT possible in case DC_1A_n41A is not still allowed. The reason is when n41 is UL, Band 1 DL is being damaged by the n41A UL.
    Example 2: DC_1A-3A_n8-n41A_UL_1A_n8A or 1A_n41A or 3A_n8A or 3A_n41A
      EN-DC of DC_1A-3A_n8A-n41A_UL_1A_n8A and 3A_n8A can be simultaneous Rx/Tx
  Hence, if simultaneous Rx/Tx is possible or not depends on possible paired UL configuration.

## Slide 6: Schedule
The outcome of discussion of which lower order configuration is simultaneous Rx/Tx mandatory affects the outcome of the higher order configuration including the lower.
RAN4 decision on which configuration shall be simultaneous Rx/Tx mandatory does not affect RAN2 capability work.
Moreover, which NR CA and EN-DC configurations will remain as Rel15 is not clear by the end of RAN4#87. Some of them may move to Rel-16.
Hence, at least in R4#87, it would be efficient for RAN4 to focus on the lowest order configuration since that outcome is the key to discuss those for higher order configurations.
The time for the final decision on RAN4#88 or 88BIS considering the number of configurations. The exact time can be discussed.

## Slide 7: Summary
Harmonic and IMD are not directly relevant to the discussion.
For EN-DC/NR CA configurations whose all the fallback modes are simultaneous Rx/Tx mandatory, those configurations are considered as simultaneous Rx/Tx to be mandatory as well.
In case a certain EN-DC/NR CA configuration has NOT simultaneous Rx/Tx mandatory fallback modes, simultaneous Rx/Tx mandatory shall be clarified for each paired UL configuration basis.
At least in R4#87, RAN4 should focus on the lowest order configuration since that outcome is the key to discuss those for higher order configurations.
The time for the final decision on which configuration shall be Rx/Tx mandatory would be RAN4#88 or 88BIS considering the number of configurations. The exact time can be discussed.