## Slide 1: Way forward on new gaps for dense PRS configuration
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #87 Busan, Korea, 21st – 25th May, 2018
Agenda item: 6.20.4.4
R4-1807365

## Slide 2: Background
More than one new measurement gap pattern are introduced to support dense PRS
  FFS wether the same gap patterns can be used for both FDD and TDD
The new measurement gap patterns are specified in 36.133
Gap pattern ID is signalled to the UE
New measurement gap patterns are characterized by:
  MGL > 6
  MGL not longer than the number of PRS subframes needed to meet RSTD requirements + 2 subframes for switching
  MGL/MGRP < X, X is TBD
UE may indicate a preferred measurement gap pattern ID
A measurement gap pattern with a longer MGL may be indicated for CEModeB and a shorter MGL for CEModeA

## Slide 3: Background
A new measurement gap pattern is configured for UE that requires such gaps for performing RSTD measurements configured via LPP
Impact on RSTD requirements:
  The existing UE Cat M1 and Cat M2 accuracy requirements for RSTD measurements in gaps shall also apply with the new gaps
New measurement gap patterns shall not be requested if UE is not configured with RSTD measurements via LPP
The new measurement gap pattern configurations are to be specified assuming X=0.15 (MGL/MGRP < X [R4-1803147])

## Slide 4: WF
New gaps shall not be used for RRM measurements.
Upon receiving RSTD measurement configuration, UE requests the proper RSTD gap pattern from the serving eNB.
Upon receiving RSTD measurement configuration with new gaps, UE should suspend or delay RRM measurement report and resume after the new gaps are no longer used.
Enhance RLM requirement as long as new gaps for dense PRS configuration are introduced.

## Slide 5: Gap patterns
Gap Pattern Id | MeasurementGap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms) | Measurement Purpose | Notes
[Rstd0] | 6 | 40 | Only catM2 5MHz CE mode A | 
[Rstd1] | 10 | 80 | Only catM2 | 
[Rstd2] | 10 | 160 | Only catM2 | 
[Rstd3] | 10 | 320 | Only catM2 | 
[Rstd4] | 10 | 640 | Only catM2 | 
[Rstd5] | 10 | 1280 | Only catM2 | 
[Rstd6] | 14 | 160 | Only CE mode A | 
[Rstd7] | 14 | 320 | Only CE mode A | 
[Rstd8] | 14 | 640 | Only CE mode A | 
[Rstd9] | 14 | 1280 | Only CE mode A | 
[Rstd10] | 24 | 160 | Only CE mode A | TDD only
[Rstd11] | 24 | 320 | Only CE mode A | TDD only
[Rstd12] | 24 | 640 | Only CE mode A | TDD only
[Rstd13] | 24 | 1280 | Only CE mode A | TDD only
[Rstd14] | 32 | 320 |  | 
[Rstd15] | 32 | 640 |  | 
[Rstd16] | 32 | 1280 |  | 
[Rstd17] | 54 | 640 |  | TDD only
[Rstd18] | 54 | 1280 |  | TDD only
[Rstd19] | 60 | 640 |  | TDD only
[Rstd20] | 60 | 1280 |  | TDD only
[Rstd21] | 64 | 640 |  | 
[Rstd22] | 64 | 1280 |  | 
Editors Note 1: the gap patterns in this table are to be down selected. Editors Note 2: gap patterns Rstd17/18 and Rstd19/20 are two options for TDD and one set of the two shall be left. Editors Note 3: consider to remove 64 MGL if 60 MGL is remained in the table. Editors Note 4: in order to introduce less patterns, consider to remove MGRP 1280. |  |  |  |