## Slide 1: WF on NR BS demod requirements and test applicability considering multiple channel bandwidths
China Telecom,
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21-24 May, 2018
Agenda: 7.12.2.1
R4-1807969

## Slide 2: Background
In LTE, 6 channel bandwidths ranging from 1.4 MHz to 20 MHz are defined, and LTE PUSCH performance requirements and some LTE PUCCH performance requirements are specified for each of the 6 channel bandwidths.
In LTE BS conformance test, for a BS supporting multiple channel bandwidths only the tests for the lowest and the highest channel bandwidth supported by the BS are applicable.

## Slide 3: Background
For NR, 3 sub-carrier spacings and 13 channel bandwidths are introduced as specified in TS 38.104.
For NR BS conformance test, the manufacturer shall declare the sub-carrier spacing and channel bandwidth that are supported by the BS under test.
Based on different operators’ needs in different regions, the supported sub-carrier spacing and channel bandwidth can be different.
  Note that roaming is not an issue to be considered for BS.
Down-selection of the sub-carrier spacing and channel bandwidth combinations should be considered, while the test coverage of BS equipment provided for different operators and regions should be guaranteed.

## Slide 4: WF
For a certain sub-carrier spacing,
  Define PUSCH/PUCCH requirements only for a sub-set of the supported channel bandwidths denoted as BW_subset = {BW1, …, BWi, BWi+1, …}.
  For PUSCH/PUCCH conformance test,
    For a BS supporting one or multiple channel bandwidths within BW_subset, only the tests for the highest supported channel bandwidth within BW_subset are applicable.
    For a BS supporting none of the channel bandwidth within BW_subset, let BW_h denote the highest channel bandwidth supported by the BS,
      Select a channel bandwidth BWi from BW_subset which satisfies that BWi < BW_h < BWi+1
      The tests for the channel bandwidth BWi are applicable. And assuming that the transmission bandwidth for channel bandwidth BWi is NRB_i, the first NRB_i PRBs within the channel bandwidth should be used for the test.
  The exact values for the set BW_subset = {BW1, …, BWi, BWi+1, …} (including the size of the set) are to be discussed in RAN4.