## Slide 1: WF on BS test applicability for different SCSes and CHBWs
China Telecom
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21-24 May, 2018
Agenda: 7.12.2.1
R4-1807969

## Slide 2: Background
In LTE, 6 channel bandwidths ranging from 1.4 MHz to 20 MHz are defined, and LTE PUSCH performance requirements and some LTE PUCCH performance requirements are specified for each of the 6 channel bandwidths.
In LTE BS conformance test, for a BS supporting multiple channel bandwidths only the tests for the lowest and the highest channel bandwidth supported by the BS are applicable.

## Slide 3: Background
For NR, 3 sub-carrier spacings and 13 channel bandwidths are introduced as specified in TS 38.104.
For NR BS conformance test, the manufacturer shall declare the sub-carrier spacing and channel bandwidth that are supported by the BS under test.
Based on different operators’ needs in different regions, the supported sub-carrier spacing and channel bandwidth can be different.
  Note that roaming is not an issue to be considered for BS.
Down-selection of the sub-carrier spacing and channel bandwidth combinations should be considered, while the test coverage of BS equipment provided for different operators and regions should be guaranteed.

## Slide 4: Background
In RAN4#87 meetings, the group has discussed the test applicability issue. One candidate solution is proposed as:
  For a certain sub-carrier spacing,
    Define PUSCH/PUCCH requirements only for a sub-set of the supported channel bandwidths denoted as BW_subset = {BW1, …, BWi, BWi+1, …}.
      The exact values in the set BW_subset = {BW1, …, BWi, BWi+1, …} (including the size of the set) are to be discussed in RAN4.
    For PUSCH/PUCCH test applicability, the following option can be considered:
      For a BS supporting one or multiple channel bandwidths, the tests for the highest supported channel bandwidth are applicable.
        Let BW_h denote the highest channel bandwidth supported by the BS
        Select a channel bandwidth BWi from BW_subset which satisfies that BWi <= BW_h < BWi+1
        Assuming that the transmission bandwidth for channel bandwidth BWi is NRB_i, the lowest or highest or middle NRB_i PRBs within the channel bandwidth should be used for the test, and the requirements for the channel bandwidth BWi are applicable.
          FFS: the lowest, highest or middle NRB_i PRBs are to be used
      FFS: whether the tests for the lowest supported channel bandwidth are applicable.
Up to now, there is no consensus on this solution

## Slide 5: WF
Down selection is needed on channel BW for each SCS to be tested. Applicability of the tests should be further discussed.
Applicability of testing for a certain SCS is based on BS declaration. If a specific BS supports multiple SCSes, the applicability rule in terms of SCS is FFS.
Companies are encouraged to provide inputs on the test applicability for different CHBWs and SCSes in the next meeting.