## Slide 1: WF on 2RX Requirements for vehicle mounted NR UE at FR1
LG Electronics, Volkswagens, General Motors, Samsung, Qualcomm Incorporated, OPPO
3GPP TSG-RAN WG4 #87 Meeting Busan, Korea, 21 - 25 May 2018 Agenda Item: 7.5.9
R4-1808169

## Slide 2: Background
In LS from 5GAA, Car OEM requested to allow 2Rx antenna as exceptional case for vehicle mounted NR UE at frequency bands where 4Rx is mandated.
  Use case is infotainment or e-call service using Uu interface
  4Rx mandating for some NR operating bands (n7, n38, n41, n77, n78, n79) at FR1 will restrict the design freedom of Car OEM.
  If exceptional 2Rx antenna is not agreed, slower deployment of vehicle mounted NR UE is expected which can result in less positive market perception of 5G.
  This exception request is not for the NR V2X service specified in SA1 in Rel-15.
    No NR V2X WI in RAN as of now.
    This issue is irrelevant with NR V2X.

## Slide 3: Issues
RAN4 list up technical aspect for 2Rx vehicle UE
  1 : Coverage issues with 4Rx Handheld device and 2Rx Vehicle UE (Huawei, CMCC, Vodafone)
    Link budget, typical RF architecture and SNR for the receiver
  2 : Need to distinguish Handheld UE and Vehicle UE in FR1? (Qualcomm, Skyworks, Vodafone, CMCC)
    Need to declare its type to TE vender?
    FFS whether RAN5 define a test case for this UE type
  3 : Demodulation / RRM impact with 2Rx vehicles (Ericsson)
  4: More information from automotive industry about the difficulty of mounting 4Rx antennae of the vehicle (Huawei, Vodafone, CMCC)

## Slide 4: WF
RAN4 recommend to have decision in RAN #80 on how to resolve this 5GAA request to have 2Rx as an exceptional case for vehicle mounted NR UE with following options
  Option1: Treated in Rel-15 TEI in Q3 2018
  Option2: treated in release independent manners from Rel-15
  Option3: treated as company CR in RAN #80
RAN4 send LS to RAN on the status of discussion
  All technical issues to be further investigated and possible solutions (including additional information from Car manufacturers on implementation) will be captured in the LS

## Slide 5: Appendix (1)
Issues
  1 : Coverage issues with 4Rx Handheld device and 2Rx Vehicle UE
  2 : Need to distinguish Handheld UE and Vehicle UE in FR1?
  3 : Demodulation / RRM impact with 2Rx vehicles
  4 : The difficulty of mounting 4Rx antennae on the roof of the vehicle
Answers
  Issue 1:
    Antenna gain [3] in Car is much higher than handheld
    DL: Taking antenna gain into account, Car with 2Rx have no less SNR than handheld device with 4Rx UE
    UL: Taking antenna gain into account, Car has superior performance than handheld device.
  Issue 2:
    UE declare its type for testing
      For RFIC GCF test, both 2Rx and 4Rx can be declared for all chipset
      For device GCF test, handheld device can only declare 4Rx
  Issue 3 :
    Demodulation/RRM with requirements applied per number of declared Rx.

## Slide 6: Appendix (2)
  Issue 4:
  Implementation difficulties include:
  Antenna connector availability
    Tighter requirements in quality & cost requirements compared to hand held UE
  Environmental requirements like water proofing antenna systems limit # of antenna slots on the roof
  Additional antenna cables – cost, space
    Room for cables through C-pillars (like Car frame) is not available
    Weight of additional cables affect the automotive design
    Low end cars have serious design restrictions, when # of C-pillars are limited
  Limited space for placement of communication modules
    Emergency call is mandated in some regions. Placement of radio modules for e-call, etc., limit the placement options for cellular antenna systems.
    Such scenarios introduce additional cabling issues within the automotive design.

## Slide 7: Appendix (3)
  Form factor of the car is limited
    Multiple antenna placements at different position, for example in roof top does not guarantee enough real estate
    Best position of antenna systems is subject to optimization for implementing best antenna radiation capabilities
  Additional RF compensator requirements to compensate loss
    Which requires space and cost. Also adds to additional heating of the automotive communication systems.
  Multiple radios in car should be considered
    Implementation challenges inside a car hold tougher requirements (similar as above) when compared to hand held UE.
  Additional heat compensation requirements (ambient/operating temperature until 95°C)
    The 5G device inside automotive must be fully functional, heat sink measures could be required when antenna chains increase within telematics control unit.
    Long term product life should be considered which is also different from hand held UE
    Qualification requirements are different and harder compared to UE hand held (Ex: drop test)
  Costs associated with points 1-8 is significant for automotive development. Cannot be considered trivial.

## Slide 8: Appendix (4)
View of Automotive Industry
  Mandating 4 RX impose serious constraints to support 5G compatible device in automotive sector.
  Working group level agreements in rel-15 will avoid the risk of automotive industry delaying adoption of 5G Sub-6 GHz technology and will enable to further enhance automotive vertical integration in 3GPP scope.
  The technology definition is recommended to be adaptive and flexible, when supportive technical and business related facts exist.
  In addition to points 1-9, OEMS request operators to share specific points where more explanation and facts from automotive development chain are necessary, with respect to RAN plenary to have agreements.

## Slide 9: Appendix (5)
C-pillars (from HYUNDAI)

## Slide 10: References
[1] R4-1806681 Consideration on 2Rx REFSNES for NR vehicular UE at FR1 [2] R4-1806682 Draft CR on REFSENS requirements for NR vehicular UE at FR1
[3] ECCREP228 (Refer Antenna gain in 2.4)
[4] http://5gaa.org/membership/our-members/
[5] LS from 5GAA to 3GPP RAN 4
[6] 3GPP TS 36.101 Chapter 7 on RX REFSENS