## Slide 1: WF on multi-band framework for FR2
Apple Inc., OPPO, LGE, Intel Corporation, vivo, Xiaomi, TCL, Spreadtrum, Asus, Kyocera, Hisense, Hytera, Meizu, IITH, IITM, CEWiT
R4-1808215
3GPP TSG-RAN WG4 Meeting #87
Busan, Korea, 21 – 25 May, 2018
Agenda item: 7.5.8.1

## Slide 2: Background
Antenna roll-off loss vs. frequency quantified the intra-band variation of peak EIRP in R4-1712319
Intra-band variation of the spherical coverage CDF was quantified, and multi-band considerations were identified in R4-1806185
A multi-band framework with ΔTMB relaxations was proposed in R4-1806136 and R4-1806138
EIRP CDF results, as summarized in R4-18xxxxx, have taken different assumptions on supported frequency ranges and collocation of the simulated/measured arrays
RAN4 has discussed the implications of multi-band support as well as how to handle this situation in the specification

## Slide 3: Multi-band framework
Current situation with FR2 bands is shown at right
Peak EIRP, peak EIS, and spherical coverage performance for UEs which support a single band vs. multiple bands is expected to be degraded
The multi-band degradation may depend on:
  Whether the metric is EIRP at beam peak or at 50%-tile CDF
  Which combination of bands the UE supports
The framework can be scalable for future bands if:
  Requirements are defined per band assuming the UE supports the single band
  Based on combinations of supported bands by the UE, appropriate relaxations for each requirement are defined

## Slide 4: Agreements (1)
RAN4 defines the multi-band framework for FR2 requirements:
  Peak EIRP, peak EIS, and spherical coverage requirements are defined per FR2 band assuming the UE supports the single band
  A table of ΔTMB relaxations defines the appropriate relaxations for each requirement as a function of the combinations of supported bands
    FFS whether ΔTMB values are the same or different for peak EIRP, peak EIS, and EIRP at 50%-tile CDF
Analysis and proposals on EIRP at 50%-tile CDF assuming the UE supports the single band are needed
A list of combinations of supported bands is needed
  One option is to use all possible combinations of NR FR2 bands
  Other options are not precluded
Analysis and proposals on ΔTMB for each of the following metrics per band and as a function of combinations of supported bands are needed:
  Peak EIRP
  Peak EIS
  EIRP at 50%-tile CDF
RAN4 aims to conclude the above open items at the earliest RAN4 WG meeting with RF agenda

## Slide 5: Agreements (2)
Existing agreements on peak EIRP, peak EIS are maintained assuming the UE supports the single band:
Peak EIRP and peak EIS requirement relaxations, ΔTMBP and ΔTMBR, are TBD
EIRP at 50%-tile CDF for UE which supports a single band:
Spherical coverage requirement relaxations, ΔTMBS, for UE which supports n257+n258+n260+n261:
The remaining ΔTMB relaxations and combinations of supported bands are TBD
Operating Band | Min Peak EIRP (dBm)
n257 | 22.5
n258 | 22.5
n260 | 20.5
n261 | 22.5
NOTE 1: Minimum peak EIRP is defined as the lower limit without tolerance | 
Operating Band | REFSENS (dBm) / Channel Bandwidth |  |  | 
 | 50 MHz | 100 MHz | 200 MHz | 400 MHz
n257 | -88.3 | -85.3 | -82.3 | -79.3
n258 | -88.3 | -85.3 | -82.3 | -79.3
n260 | -85.7 | -82.7 | -79.7 | -76.7
n261 | -88.3 | -85.3 | -82.3 | -79.3
Operating Band | ΔTMBS (dB) | EIRP at 50%-tile CDF (dBm)
n257 | 2.5 | 8.0
n258 | 2.5 | 8.0
n260 | 2.5 | 4.0
n261 | 2.5 | 8.0
Operating Band | EIRP at 50%-tile CDF (dBm)
n257 | 10.5
n258 | 10.5
n260 | 6.5
n261 | 10.5
NOTE 1: Minimum EIRP at 50%-tile CDF is defined as the lower limit without tolerance |