## Slide 1: New work split between RAN4 and RAN5 on NR UE specifications (38.101-1/2/3/4)
Agenda Item: 7.5.10, 7.12.1
Source: Ericsson
Document for: Approval
3GPP TSG-RAN WG4 Meeting #87
Busan, 21st– 25th May, 2018
R4-1808237

## Slide 2: Background
The RMC related test parameters are not taken as high priority in RAN4 as they are more testing related and specified in Annex, instead of specified in core spec with specific chapters.
Many issues identified by RAN5 related to RMC
    For eLAA RAN4 missed to define UL RMCs
    For NB-IoT RMC for RF tests with LS from RAN5 RP-162346 where the scheduling information for UL and DL sub-frame configuration in NB-IoT RMC is missing from RAN4 spec.
      For NB-IoT RAN4 did not specify scheduling patterns RAN5 was expecting which caused delays
    NR FR1 the UL RMC and OCNG patterns are still missing and not discussed in RAN4 even as indicated in RAN5 LS R5-182094.
Annex A (and some other Annexes) is formative so once anything is missing in RAN4 spec it will bring a direct impact as serious delay for RAN5 core work.

## Slide 3: General idea on how to avoid future delay
RAN4 keeps the responsibility of setting up UE RF/performance requirements
    All the essential parameters (as examples referred to current LTE UE spec 36.101 with all the test parameters specified in Tables in Chapter 6, 7, 8, 9, 10) should be still kept in RAN4 NR UE spec (38.101-1/2/3/4).
    Alignment among companies for RF/performance requirements is kept in RAN4
Some testing related parameters (non-performance critical parameters) can be shifted to RAN5, if the capacity in RAN5 allows, in order to avoid any unnecessary delay for future NR work
    Mainly some Annexes such as RMC and OCNG patterns
    How to decide which parts could be taken over by RAN5 should be based on group discussions by both RAN4 and RAN5. (Joint session is preferred)
      Propose to go through Annex in LTE UE spec 36.101 as example for NR work.
      Following slides bring an initial thought on how to split the work of Annex by taking LTE UE spec 36.101 as example

## Slide 4: Annex A in 36.101 (Detailed parameters moved to RAN5?)
A.1 General
A.2 UL RMC
A.3 DL RMC
A.4 CSI RMC
A.5 OCNG patterns
A.6 Sidelink RMC
A.7 Sidelink reference resource pool config
A.8 V2X RMC
A.9 V2X reference resource pool config

## Slide 5: Annex B in 36.101(Kept in RAN4)
B.1 Static channel
B.2 Multi-path fading channel
  MIMO channel models
B.3 HST channel
B.4 Beamforming model
B.5 Interference model for Type A receiver
B.6 Interference model for Type B receiver
B.7 Interference model for Control channel Type A and Type B receiver
B.8 Burst transmission models for LAA

## Slide 6: Annex C-E in 36.101
C: Downlink Physical Channels (Detailed parameters moved to RAN5?)
  C.1 General
  C.2 Set-up
  C.3 Connection
    Measurement of performance requirement (Power allocation)
D: Characteristics of the interfering signal (Kept in RAN4 but moved to the other parts (core test parts or subclause in Annex B) instead of one standalone chapter as Annex D)
  D.1 General
  D.2 Interference signals
E: Environmental conditions (Kept RAN4)
  E.1 General
  E.2 Environmental
    E.2.1 Temperature
    E.2.2 Voltage
    E.2.3 Vibration (To be removed? since it’s not tested in RAN5)

## Slide 7: Annex F-H in 36.101
F: Transmit modulation (Kept in RAN4)
  F.1 Measurement Point
  F.2 Basic Error Vector Magnitude measurement
  F.3 Basic in-band emissions measurement
  F.4 Modified signal under test
  F.5 Window length
  F.6 Averaged EVM
  F.7 Spectrum Flatness
G: Reference sensitivity level in lower SNR (Informative. To be removed in NR spec?)
H: Modified MPR behaviour (Kept in RAN4 but to be discussed how to specify it for NR?)

## Slide 8: Challenge for NR spec 38.101-1/2/3/4 Annex
UE RF and Perf have separated spec for 38.101 so we can’t really keep the same Annex index as LTE in any case
Any common parts e.g. channel models, interference models, test models between UE RF and performance should be duplicated in the Annexes in all 38.101-1/2/3/4, regardless Annex A (RMC and OCNG) ends in RAN4 or RAN5 specs.

## Slide 9: Example of chapter 7 REFSENS test with new work split
REFSENS tests refer to DL full RB allocation and UL partial RB allocation.
From test in Chapter 7, remove the reference of Annex on RMC and OCNG
    7.3.1 Minimum requirements (QPSK)
    The throughput shall be ≥ 95% of the maximum throughput of the reference measurement channels as specified in Annexes A.2.2, A.2.3 and A.3.2 (with one sided dynamic OCNG Pattern OP.1 FDD/TDD for the DL-signal as described in Annex A.5.1.1/A.5.2.1) with parameters specified in Table 7.3.1-1 and Table 7.3.1-2 and Table XXX(new table for per-slot based parameters and target code rate)
  Table 7.3.1A-0bF: Uplink configuration for reference sensitivity (exceptions due to cross band isolation issues of TDD and FDD bands) should be kept in RAN4 spec as reference for UL resource allocation

## Slide 10: Per-slot based test parameter table defined in RAN4 spec to derive RMC
This table is additional to the general test parameter table, to derive RMC (could be potentially merged into one table as test parameters)
    Modulation order
    Targeted code rate
    TDD UL/DL config slot pattern
    Number of HARQ process
    Max HARQ transmission
    RB allocation type (Full RB allocation or Partial load on which RBs)
    PDSCH start symbol

## Slide 11: DL RMC table suggested to move to RAN5?
For each bandwidth/SCS/RB allocation/targeted code rate
    MCS index
    Information Bit Payload per Slot
    Transport block CRC
    LDPC base graph
    Number of Code Blocks per Slot
    Binary Channel Bits per Slot
    Max. Throughput averaged over 1 frame

## Slide 12: UL RMC table suggested to move to RAN5?
For each bandwidth/SCS/RB allocation/targeted code rate
    DFT-s-OFDM Symbols per slot
    MCS index
    Payload size
    Transport block CRC
    LDPC base graph
    Number of Code Blocks per Slot
    Total Number of Bits per Slot
    Total Symbols per Slot

## Slide 13: OCNG patterns suggested to move to RAN5?
All OCNG definition and tables
    FDD/TDD
    One side/Two sides

## Slide 14: Way forward
RAN4/RAN5 discuss the possibility of moving the responsibility of parts of Annex of 38.101 (e.g. RMC and OCNG) to RAN5, with the intention to avoid delay in RAN5 for future NR work, as proposed in Page 3 joint session is preferred.
    In practice if possible, RAN4 will decide per slot based test parameters to derive the RMC and brings examples on how to define the RMC by proper calculations.
    If not RAN4/RAN5 should discuss jointly what’s the practical timeline to finalize all left in RAN4 and deliver to RAN5

## Slide 15
http://www.3gpp.org/ftp/TSG_RAN/WG4_Radio/TSGR4_87/Docs/R4-1808237.zip