## Slide 1: WF on test cases for NR conformance testing
Huawei, Ericsson, Nokia, ZTE
3GPP TSG RAN WG4 #87 R4-1808318
Busan, Korea, 21-24 May, 2018

## Slide 2: Background
Referrence
  R4-1807879 Test cases limitation for NR conformance testing, Nokia, Nokia Shanghai Bell
  R4-1807529 Test cases for NR Huawei, HiSilicon

## Slide 3: Way forward- test cases
Agreements for reduction of BS NR conformance test cases,
  Modulation scheme for EVM requirement:
    For supported modulation orders without power back off, the EVM limit should be tested only at the highest modulation order.
    For the supported modulation order(s) with power back off declared by BS vendor, the EVM limit should be tested only at the highest modulation order(s) with same reduced output power.
  RF channels B (bottom), M (middle) and T (top)
    Down-selection of RF channels B (bottom), M (middle) and T (top) should be considered case by case.