## Slide 1: Handling of receiver requirements in EN-DC
Qualcomm
3GPP TSG-RAN WG4 Meeting #88 R4-1811465
Gothenburg, Sweden, 20th – 24th Aug, 2018

## Slide 2: Background
Receiver requirements as discussed in R4-1811027 are unclearly or not specified in TS 38.101-3
Agreements:
  Proposal 1: RAN4 will discuss and agree receiver requirement handling for EN-DC mode in following meeting and dedicated agenda item will be opened.
  Proposal 2: RAN4 will inform RAN5 that RAN4 will conclude the receiver requirements in the RAN4#88Bis and #89
RAN5 needs clarifications on what and how to test these missing requirements
Discussion indicated that treatment of inter-band and intra-band could be different

## Slide 3: WF for general requirement handling in 38.101-3
Stand Alone Transmitter and Receiver requirement in TS 38.101-1 and TS 38.101-2 are applied unless exceptions are specified in TS 38.101-3.
Situation will be clarified in TS 38.101-3 with statement in section 7.1:
  Unless otherwise stated, requirements for NR receiver written in TS 38.101-1 and TS 38.101-2 apply and are assumed anchor agnostic. Requirements are verified under conditions where anchor resources do not interfere NR operation
Similarly for section 6.1 for transmitter:
  Unless otherwise stated, requirements for NR transmitter written in TS 38.101-1 and TS 38.101-2 apply and are assumed anchor agnostic. Requirements are verified under conditions where anchor resources do not interfere NR operation

## Slide 4: Way Forward for EN-DC inter-band
For UE’s that do support SA, requirements are verified in SA mode for NR and performance is assumed to be EN-DC combination agnostic
For UE’s that do not support SA i.e. they can only establish connection with the help from LTE anchor, requirements can be verified by either of two methods:
  1) choosing an anchor band and channel that does not interfere with NR performance or
  2) (preferable method) by first establishing connection and then disabling all resources from anchor RAT, meaning DL/UL scheduling and SRS/CQI disabled and this way ensuring presence of anchor does not interfere NR performance

## Slide 5: Way Forward for EN-DC intra-band
SA mode requirements may not be applicable if UE is configured for EN-DC
Intra-band receiver requirements will be defined for EN-DC mode