## Slide 1: WF on Transmitter in-band TRP emissions (wanted and unwanted)
Ericsson, R4-1811674

## Slide 2: General
In band TRP based requirements OTA MUs are higher than the corresponding conducted MUs, assuming the following:
  MU calculation is presented in the TR as an MU budget, including a consensus view on instrument setup uncertainty
  The TS shall contain a sentence clarifying that it may be possible to design OTA setups that achieve a lower MU that the one indicated in the specification; in such cases the lower MU may be considered when assessing requirement compliance.
    (In addition to the existing description of test setups with higher MU)

## Slide 3: EIRP accuracy
Existing values:
  0-3 GHz: 1.0dB
  3-4.2GHz: 1.2dB
Frequency flatness term impacts existing values
Proposed value for 0-2: 1.1dB, 3-4.2: 1.3dB, 4.2-6GHz: 1.3dB
MU budget for 4.2-6GHz is shown in the spreadsheet
TT = MU

## Slide 4: BS output power
Company MU views:
  0-3GHz: 1.2 (Hua), 1.3 (Eri), 1.9 (Nokia)
  3-4.2GHz: 1.4 (Hua, Eri), 2.0 (Nokia)
  4.2-6GHz: 1.4 (Eri), 2.0 (Nokia)
The main issue driving the difference between the Nokia and Eri/Hua numbers is whether the SE is treated as 1 sigma or 2 sigma
Proposal: Treat SE as 2 sigma
Proposed MU: 0-3GHz: 1.4dB 3-4.2GHz: 1.5dB, 4.2-6GHz: 1.5dB
MU budget is captured in the spreadsheet
TT = MU

## Slide 5: Relative ACLR
Company MU views:
  0-3GHz: 1.2 (Hua), 1.0 (Eri), 0.9 (DCM)
  3-4.2GHz: 1.3 (Hua, DCM), 1.1 (Eri)
  4.2-6GHz: 1.1 (Eri), 1.4 (DCM)
Values are pretty close
Proposed values:
  1.0 for 0-3GHz, 1.2 for 3-6GHz
  MU values apply for all eAAS and NR FR1 channel bandwidths
Uncertainty budget captured in the spreadsheet
TT = MU

## Slide 6: OBUE and SEM
Company views on MU:
  0-3GHz: 1.9 (HW), 1.3 (Eri), 1.2 (DCM)
  3-4.2GHz: 2.3 (HW), 1.4 (Eri, DCM)
  4.2-6GHz: 1.4 (Eri), 1.5 (DCM)
The main issue leading to the difference between the HW and DCM/Eri numbes is the treatment of the instrument uncertainty
Proposed values:
  0-3GHz: 1.8dB, 3-4.2GHz: 2.0dB, 4.2-6GHz: 2.0dB
MU budget is captured on the following slide
TT=MU for 0-10MHz, TT=0dB for >10MHz

## Slide 7: Absolute ACLR
Company views on MU:
  0-3GHz: 2.4 (HW), 1.3 (Eri), 1.2 (DCM)
  3-4.2GHz: 2.9 (HW), 1.4 (Eri, DCM)
  4.2-6GHz: 1.4 (Eri), 1.5 (DCM)
The main issue leading to the difference between the HW and DCM/Eri numbes is the treatment of the instrument uncertainty
Proposed MU:
  0-3GHz: 2.2dB, 3-6GHz 2.7dB
TT = 0dB