## Slide 1: Tx/Rx TRP spurious emissions TT
Huawei
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20th – 24th Aug 2018
R4-1811672

## Slide 2: Back ground
The MU values have been agreed in R4-1811672
TX mandatory emissions (CAT A/B)
  30 MHz ≤ f ≤ 6 GHz, MU=2.3dB
  6 GHz < f ≤ 19 GHz, MU=4.2dB
Receiver spurious emissions
  30 MHz ≤ f ≤ 6 GHz, MU=2.5dB
  6 GHz < f ≤ 19 GHz, MU=4.2dB
Additional requirements- co-existence
  f ≤ 3 GHz, MU=2.5dB
  3 GHz < f ≤ 4.2 GHz, MU=2.5dB
    4.2 GHz < f ≤ 6 GHz, MU=2.9dB

## Slide 3: TT values
The MU values have been agreed in R4-1811672
TX mandatory emissions (CAT A/B)
  TT=0
Receiver spurious emissions
  TT=MU
Additional requirements- co-existence
  For 3GPP to 3GPP co-existence, TT=MU
    UTRA - Tables 9.7.6.3.3-1, 9.7.6.3.3-3
    E-UTRA – tables: 9.7.6.4.3.2-1, 9.7.6.4.3.2-5, 9.7.6.4.3.2-6, 9.7.6.4.3.2-7, 9.7.6.4.3.2-8)
  For PHS, TT=0
    UTRA – Tables 9.7.6.3.3-2
    E-UTRA – tables: 9.7.6.4.3.2-2
  For public safety, TT=0
    UTRA – Tables 9.7.6.3.3-4, 9.7.6.3.3-5
    E-UTRA – tables: 9.7.6.4.3.2-2-3, 9.7.6.4.3.2-2-4, 9.7.6.4.3.2-9, 9.7.6.4.3.2-10