## Slide 1: WF Interruption requirements for UL carrier addition-release via RRC in NR
RAN4#88, Gothenburg, Sweden R4-1811683

## Slide 2: Background
Agreed interruptions for inter-band cell add-release
When one SCell is added or released
  an interruption on PSCell: of up to X1 slot, if the PSCell is not in the same band as any of the SCells being added or released
  an interruption on any activated SCell in SCG: of up to X1 slot, if the activated SCell is not in the same band as any of the SCells being added or released
 | NR Slot length (ms) | Interruption length X1 slot |  | Interruption length Y1 slotNote 1
 |  | Sync | Async | 
0 | 1 | 1 | 2 | 1
1 | 0.5 | 2 | 3 | 2
2 | 0.25 | 5 |  | 4
3 | 0.125 | 9 |  | 8

## Slide 3: Current agreement on UL carrier/add relase
From 38.133
When an UL carrier or supplementary UL carrier is configured or deconfigured, an interruption on LTE PCell, all activated LTE SCells, PSCell and all activated SCells within the same FR as the reconfigured uplink carrier of up to [1] slot, is allowed immediately after the RRC reconfiguration procedure [2].
Issues with the current agreement
  Length of interruption
  Location of interruption

## Slide 4: Interruption length
From UE perspective an UL carrier reconfiguration can potentially have the same impact on other cells as a cell add/release
  An UL carrier add may cause additional spurs which may necessitate the re-programming of existing RF chains
Proposal: Interruption duration should be aligned with that for carrier add/release

## Slide 5: Location of interruption
Current specification says interruption can be take immediately after RRC reconfiguration
As is in the case of cell add/release, the RF programming of the UL carrier and the possible re-configuration of existing cells would need to take place during RRC re-configuration
  Thus interruption would be needed during the re-configuration
Proposal: Interruption should be allowed during RRC re-configuration