## Slide 1: 3GPP TSG-RAN WG4 Meeting #88 Gothenburg, Sweden, 20 - 24 Aug 2018
Huawei, …
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1811727

## Slide 2: Background
R4-1808025 Way forward on PUCCH demodulation requirements, RAN4#87
R4-1809556 Way forward for NR PUCCH demodulation performance requirements, RAN4#1807

## Slide 3: PUCCH Requirements
Define PUCCH performance requirements with 1Tx in Rel-15
Hopping
  Intra-slot frequency hopping: enable
    Option1:
      startingPRB = 0
      secondHopPRB = the largest PRB index – nrofPRBs
    Option 2:
      startingPRB = 2
      secondHopPRB = the largest PRB index – nrofPRBs -2
  hoppingId = 0

## Slide 4: Simulation assumption for format 0
Test scenarios: (Number of bits, Number of OFDM symbols, Number of PRB):
  (1, 1, 1)
  (1, 2, 1)
initialCyclicShift = 0
For FR1
  startingSymbolIndex = 13 for 1 OFDM symbol
  startingSymbolIndex = 12 for 2 OFDM symbols
For FR2
  Option 1:
    startingSymbolIndex = 13 for 1 OFDM symbol
    startingSymbolIndex = 12 for 2 OFDM symbols
  Option 2:
    startingSymbolIndex = 11 for 1 OFDM symbol
    startingSymbolIndex = 10 for 2 OFDM symbols
Test metric
    DTX to Ack probability <1%
    Missed Ack probability < 1%

## Slide 5: Simulation assumption for format 1
Test scenarios: (Number of bits, Number of OFDM symbols, Number of PRB):
  (2, 14, 1)
initialCyclicShift = 0
startingSymbolIndex = 0
The index of the orthogonal sequence i=0
Test metric
    DTX to Ack probability <1%
    [Missed Ack probability < 1%]
    NACK2ACK probability < 0.1%

## Slide 6: Simulation assumption for format 2
Test Scenarios: (Number of bits, Number of symbols, Number of PRBs)
  (4, 1, 4)
  (22, 2, 9)
For FR1
  startingSymbolIndex = 13 for 1 OFDM symbol
  startingSymbolIndex = 12 for 2 OFDM symbols
For FR2
  Option 1:
    startingSymbolIndex = 13 for 1 OFDM symbol
    startingSymbolIndex = 12 for 2 OFDM symbols
  Option 2:
    startingSymbolIndex = 11 for 1 OFDM symbol
    startingSymbolIndex = 10 for 2 OFDM symbols
Test metric
  If number of bits <= 11
    DTX to Ack probability <1% and Missed Ack probability < 1%
    FFS NACK2ACK < 0.1%
  If number of bits > 11: BLER < 1%

## Slide 7: Simulation assumption for format 3
Test Scenarios: (Number of bits, Number of symbols, Number of PRBs)
  (16, 14, 1)
  (16, 4, 3)
DMRS pattern:
  FR1:
    Without additional DMRS for all cases
    With additional DMRS for cases with the number of OFDM symbols more than 9
  FR2:
    Without additional DMRS
    FFS with additional DMRS
Modulation: QPSK; FFS for pi/2 BPSK
startingSymbolIndex = 0
Test metric: BLER < 1%

## Slide 8: Simulation assumption for format 4
Test scenarios: (Number of bits, Number of OFDM symbols, Number of PRBs):
  (22, 14, 1)
DMRS pattern:
  FR1: with and without additional DMRS
  FR2:
    Without additional DMRS
    FFS with additional DMRS
Modulation: QPSK
startingSymbolIndex = 0
occ-Length = n2
occ-Index = n0
Test metric: BLER < 1%

## Slide 9: Initial Simulation Assumptions
Parameters |  | PUCCH Format 0 | PUCCH Format 1 | PUCCH Format 2 | PUCCH Format 3 | PUCCH Format 4 | 
BandWidth/SCS |  | FR1: 10MHz/15kHz; 40MHz/30kHz; FR2: 100MHz/60kHz; 100MHz/120kHz |  |  |  |  | 
Antenna |  | 1T2R |  |  |  |  | 
Propagation condition |  | FR1: TDL-A 30ns 10Hz; FR2: [AWGN] |  |  |  |  | 
Carrier frequency (GHz) |  | FR1: 4GHz; FR2: 30GHz |  |  |  |  | 
(#Bits, #Symbols, #PRBs) |  | (1, 1, 1) (1, 2, 1) | (2, 14,1) | (4, 1, 4) (22, 2, 9) | (16, 14, 1) (16, 4, 3) |  | (22, 14, 1)
DMRS pattern |  |  |  |  | FR1: Without additional DMRS for all cases With additional DMRS for cases with the number of OFDM symbols more than 9 FR2: Without additional DMRS |  | 
Modulaiton |  |  |  | QPSK | QPSK |  | QPSK
initialCyclicShift |  | 0 | 0 |  |  |  | 
StartingSymbolIndex |  | FR1: 13 for 1 symbol; 12 for 2 symbols; FR2: Option 1: 13 for 1 symbol; 12 for 2 symbols; Option 2: 11 for 1 symbol, 10 for 2 symbols | 0 | FR1: 13 for 1 symbol; 12 for 2 symbols; FR2: Option 1: 13 for 1 symbol; 12 for 2 symbols; Option 2: 11 for 1 symbol, 10 for 2 symbols | 0 |  | 0
Index of orthogonal sequence (time-domain-OCC) |  |  | 0 |  |  |  | 
occ-Length |  |  |  |  |  |  | n2
occ-Index |  |  |  |  |  |  | n0
Test metric | DTX to Ack probability <1% | √ | √ | √ for bits <=11 | × |  | ×
 | Missed Ack probability < 1% | √ | [ √ ] | √ | × |  | ×
 | NACK2ACK < 0.1% | × | √ | FFS for bits <=11 | × |  | ×
 | BLER < 1% | × | × | √ for bits >11 | √ |  | √