## Slide 1: WF on Intra-Band EN-DC Power Back-off Design
3GPP TSG-RAN WG4 Meeting #88 R4-1811797 Gothenburg, Sweden, 20th - 24th August 2018
MediaTek

## Slide 2: Background
Issue: Conflict in intra-band EN-DC UE assumptions between RAN4 and RAN1.
  R4-1805761, “WF for UE RF AH specific for DC_(n)71B”:
    Define two sets of A-MRP. One A-MPR(1) for case that LTE and NR modems know each other’s allocation and another A-MPR(2) for the case that LTE and NR modems do not know each other’s allocation.
  R1-1807974, “Reply LS on RAN4 agreement on intraband EN-DC A-MPR”:
    The basic design principle for the RAN1 power control agreements was that LTE processing times in EN-DC are the same as in LTE CA and LTE DC, while NR processing times are faster and therefore either the calculation of transmission power for LTE cannot take into account the RB allocation(s) of simultaneous NR transmission(s), or the calculation of transmission power for LTE cannot take into account both the presence and RB allocation(s) of simultaneous NR transmission(s), at least in the following cases:
      when the NR grant is less than 4ms in advance
      …
Whether and how power back-off design can be revised are discussed in this meeting

## Slide 3: Possible Solutions
Solution | Power back off design for type-1 UE | To be determined
Delay NR (R1-1809102) | Existing | 
LTE-only A-MPR , NR A-MPR determined by present EN-DC table and scale/drop NR if needed (R4-1811252) | Changed to new (Leave LTE as is) | Condition for drop NR
Pcmax for EN-DC (R4-1810058) | Changed to new (Leave LTE as is) | Whether additional power back-off required
Additional relaxation using e.g. either P-MPRNR (R4-1810422) or new additional A-MPR requirements | Existing + new (Up to UE selection and UE capability signaling) | Amount for the new power back-off

## Slide 4: Proposal 1
For intra-band EN-DC and type-1 UE, RAN4 decide one of the following options to move forward:
Option 1: Keep present A-MPR power back-off design
  Accommodate RAN4 original assumption, LTE and NR modems know each other’s allocations, by, e.g., delayed NR network or faster UEs
Option 2: Change A-MPR power back-off design
Option 3: Additional A-MPR power back-off design(s) with UE signaling to select and apply one
  New UE capability signaling of X bits to be agreed
Note: Other options are not precluded.

## Slide 5: Proposal 2
Other than option 1, companies are encouraged to provide new design for other options with analysis/simulation results accordingly.
  System performance impacts including UL coverage impacts
  Following earlier agreed assumptions for the UE
  MPR/AMPR/ACLR/IMD are to be characterized