## Slide 1: WF for NR PC2 fallback
Qualcomm Incorporated, Oppo
3GPP TSG RAN WG4 #88
Gothenburg, Sweden, August 20 - 24, 2018
R4-1811801

## Slide 2: Background
Option 1: Remove “may” (change to “shall”)
  Mandates that UE always falls back to PC3 when MaxUplinkDutyCycle is exceeded, even if the UE can meet SAR at PC2
Option 2: Retain “may”
  Ill-defined requirement; UE behavior is not well defined

## Slide 3: Objectives
Need to find a way to allow a UE to meet SAR under high power/ high duty cycle condition
Do not mandate that the UE reduce power unnecessarily
Need to define unambiguous requirement

## Slide 4: Proposal
The feasibility of the following way is studied in the future meeting.
  Modify the MPR definition for PC2 to increase by 3 dB when the percentage of uplink symbols exceeds the signaled capability
  MPR allows 3 dB additional power backoff as needed to meet SAR for high power/high duty cycle transmissions
  MPR is unambiguously defined
  MPR is a maximum power reduction so the UE doesn’t have to take the entire MPR if it doesn’t have to

## Slide 5: Spec change to MPR clause 6.2.2
For a power class 2 capable UE operating in Band n41, n77, n79 and n79
  when the field of UE capability maxUplinkDutyCycle is absent and the percentage of uplink symbols transmitted in a certain evaluation period is larger than 50% or
  When the field of UE capability maxUplinkDutyCycle is present and the percentage of uplink symbols transmitted in a certain evaluation period is larger than maxUplinkDutyCycle as defined in TS 38.331 (The exact evaluation period is no less than one radio frame)
  MPR defined in Table 6.2.2-2 is increased by 3 dB
Other similar spec changes (i.e., Pcmax) are also needed