## Slide 1: WF on Evaluation for 2 RX exception in Rel-15 vehicle mounted UE
Volkswagen AG,LG Electronics, Samsung, General Motors, [Skyworks], [Vodafone], [Huawei]
3GPP TSG RAN WG4 Meeting #88
Gothenburg, SE, 20th – 24th Aug, 2018 Agenda Item: 10.3
R4-1811839

## Slide 2: Background (1)
In LS from 5GAA [1], Car OEM requested to allow 2Rx antenna as exceptional case for vehicle mounted NR UE at frequency bands where 4Rx is mandated.
  Use cases are broadband use cases like infotainment or data exchange using Uu interface
  4Rx mandating for some NR operating bands (n7, n38, n41, n77, n78, n79) at FR1 will restrict the design freedom of Car OEM.  need for 2Rx vehicle UE at above listed bands
  If exceptional 2Rx antenna is not agreed, slower deployment of vehicle mounted NR UE is expected which can result in less positive market perception of 5G.
  This exception request is not for the NR V2X service specified in SA1 in Rel-15.
    This issue is irrelevant with NR V2X study in RAN1.
  RAN4 #87 agreed WF with three candidate options [2]

## Slide 3: Background (2)
RAN plenary agreed to study on evaluation for 2Rx exception in rel-15 vehicle NR mounted UE in RP-181467 with these objectives
  Aspects to study in allowing 2 RX exception for vehicle mounted UEs in frequency bands where 4 Rx is mandated:
    Investigate the impact of 2Rx vehicle mounted UE on coverage and throughput and the possible ways to avoid or at least minimize such impact.
      Link budget with 2 RX vehicular UE
      TCU receiver RF chain and architecture
      Coverage and throughput impacts at system level
    Methods to distinguish vehicular UE from handheld UE
      Methods to define vehicle mounted UEs
      Methods to verify conformance and GCF certification (excluding OTA scope)
LS from 5GAA [3] provided typical antenna gain of vehicle mounted UE.

## Slide 4: Offline Summary
Coverage and Capacity
  Coverage is more important than capacity : Agreed
    Proposal to remove capacity analysis
  Coverage is based on link budget analysis : Agreed
    Parameters for link budget needs to be agreed in this meeting
  Capacity is based on system simulation : Agreed
    Reuse RAN1 system simulation assumption as much as possible (TR38.901)
      Other prominent antenna mount location for 2Rx solutions are considered further
    Parameters for system simulation needs to be agreed in this meeting
  Values of antenna gain from 5GAA LS is used for both coverage and capacity
UE type distinction
  UE declaration is enough (OPPO)
    Not enough and Send LS to RAN5/GCF to confirm this (Huawei)
  MIMO layer signaling (LG)
  Additional signaling for UE type? (VDF..)
    Main reason for this is not to allow 2Rx Handheld UE in the network
Notes: R4-1811528 LS from 5GAA for rel-15 2 RX vehicle mounted UE
R4-1809930 Coverage related issues for 2Rx RF requirements of vehicle mounted NR UE as exception case, Samsung, LG Electronics, Volkswagen AG, Toyota InfoTechnology Center
RP-181117, Minimum requirement of 2Rx antennas for permanently mounted UE in vehicles for NR , 3GPP TSG-RAN Meeting #80

## Slide 5: WF : Parameters for Coverage
Link budget based analysis should be assumed
  Ref. : [4] R4-1809930, Coverage related issues for 2Rx RF requirements of vehicle mounted NR UE as exception case, Samsung
  Any other parameters?
    Ant. Gain of device /Body loss /Cable loss/Diversity gain
  Deployment Scenario?
    HH
      4Rx HH outdoor
      4Rx HH in-vehicle
    Vehicle
      2Rx V outdoor
  Reference bands
    n7 and n41
Notes: R4-1811528 LS from 5GAA for rel-15 2 RX vehicle mounted UE
R4-1809930 Coverage related issues for 2Rx RF requirements of vehicle mounted NR UE as exception case, Samsung, LG Electronics, Volkswagen AG, Toyota InfoTechnology Center
RP-181117, Minimum requirement of 2Rx antennas for permanently mounted UE in vehicles for NR , 3GPP TSG-RAN Meeting #80

## Slide 6: WF : Parameters for Capacity
Selection of parameters for the evaluation (e.g. losses, frequency, etc. ), Proposal:
  Losses: body, cable, etc. TBD
  reference bands are n7 and n41 (only available implementations)
Selection of evaluation scenarios. Proposals are
  1 scenario for coverage  link budget analysis
  1 scenario for capacity  evaluate system level simulation [6]
    Discussed deployment scenarios:
      Case1 : reference 80% 4Rx HH UE (indoor) + 20% 4Rx HH UE (outdoor)
        Target : 80% 4Rx HH UE (indoor) + 20% 2Rx V UE (outdoor)
      Case2 : reference 80% HH UE (indoor) + 20% 4Rx HH UE (in-vehicle)
        Target: 80% 4Rx HH UE (indoor) + 20% 2Rx V UE (outdoor)
    Channel type selection  Urban Macro (ISD=500m) in TR38.901
    Other scenario characteristics ( speed,..)  utilize the values in Annex
Decision on the measure/thresholds for the 2Rx exception for vehicular mounted UEs

## Slide 7: WF: Methods to distinguish UE type
Problem statement:
  Description/clarification of the reasons for the need for declaration of the UE type:
    Conformance tests, certification tests, network operation/optimization reasons etc.
Solution based on the problem statement
  Development of a solution/method to distinguish the UE type
  Clarification of the involvement of other groups (RAN2 : adding signaling issues in rel-15)
    Signaling option can be considered when the necessity of this signaling is clearly understood in NW perspective.
Options to distinguish UE type
  Option1: UE declaration for testing
  Option2: use MIMO layer signalling (defined the UE capability signalling as optional feature in NR)

## Slide 8: WF : Schedule/Roadmap
RAN4 #88
  High level agreement on
    Coverage related assumption
      Antenna gain
    Capacity related evaluation assumption for the performance part
      Decide reference scenario among Case 1 ~ 3
      Clarification on the decision/exception on the threshold of target
    UE type distinction
      Potential options among Option 1 ~ X
RAN4 #88Bis
  Initial simulation on capacity & coverage
  Complete UE type distinction method
    Decision on the necessity of new signaling
    If yes, send LS to RAN2 on RAN4 decision
RAN4 #89
  Complete evaluation for capacity/coverage
  LS to RAN Plenary on the conclusion

## Slide 9: Annex
Basic parameter for evaluation of system capacity
  Urban Macro (ISD=500m) in TR38.901
    FTP traffic model
    Velocity : 3km/h for both Vehicle UE and HH UE
    Pathloss model : Follow TR38.901
    Receiver type : Follow TR38.901
  UE deployment scenarios
    Case1 : reference 80% 4Rx HH UE (indoor) + 20% 4Rx HH UE (outdoor)
      Target : 80% 4Rx HH UE (indoor) + 20% 2Rx V UE (outdoor)
    Case2 : reference 80% HH UE (indoor) + 20% 4Rx HH UE (in-vehicle)
      Target: 80% 4Rx HH UE (indoor) + 20% 2Rx V UE (outdoor)
  Ant. Configuration
    HH UE : 4Rx UE with -8dBi antenna gain including cable loss
    V-UE : If agreed as reference as in Case 2, we can ask car OEMs on 4Rx antenna gain of vehicle
    V-UE : 2Rx UE with -4dBi antenna gain including cable los
  Loss for HH
    Body loss : [8] dB
    Penetration loss : [20] dB (Indoor), [15] dB(in-vehicle)

## Slide 10: References
[1] R4-1806142, LS from 5GAA on minimum number of RX antennae for NR vehicular Ues
[2]R4-1808169 WF on 2Rx requirements for vehicle mounted NR UE, LG Electronics
[3] R4-1811528, LS from 5GAA for rel-15 2 RX vehicle mounted UE
[4] R4-1809930, Coverage related issues for 2Rx RF requirements of vehicle mounted NR UE as exception case, Samsung
[5] RP-181117, Minimum requirement of 2Rx antennas for permanently mounted UE in vehicles for NR, Volkswagen AG
[6] TR38.901