## Slide 1: Way forward on gap sharing for measurement prioritization in different scenarios
Samsung, NTT DoCoMo, Verizon Wireless, KDDI, Intel, Ericsson
R4-1811854
3GPP TSG-RAN WG4#88 Meeting
Gothenburg, Sweden, Aug 20-24, 2018
Agenda: 7.4.2

## Slide 2: Background
In current TS38.133, measurement gap sharing is applicable when UE need to perform gap-based intra-frequency measurement (gap is needed or when SMTC configured for intra-frequency measurement are fully overlapping with measurement gaps), and to perform inter-frequency measurement.
  Scaling factor for intra-freq. measurement/cell identification delay: Kintra = 1 / X * 100
  Scaling factor for inter-freq. measurement/cell identification delay: Kinter = 1 / (100 – X) * 100
Network signaling ParameterName (to be determined by RAN2) | Value of X (%)
‘00’ | Equal splitting
‘01’ | [25]
‘10’ | [50]
‘11’ | [75]

## Slide 3: Problem for Intra-/Inter-Freq Gap Sharing
Based on current definition of gap sharing, UE should share per UE gap or per FR gap for FR1 among NR intra-freq, NR inter-freq, LTE inter-freq and other inter-RAT measurements.
Considering different NR deployment scenarios (EN-DC, NE-DC, NR CA, NR-NR DC) by applying current gap occasion sharing mechanism, the frequency layer which matters mobility performance can not be prioritized:
  In EN-DC case, LTE inter-frequency measurement (for inter-freq HO) needs to be prioritized than NR intra-frequency gap-based measurement, NR inter-frequency measurement, and other inter-RAT measurements (other RATs).
  In NE-DC case, NR intra-frequency gap-based measurement corresponding to NR serving cells in FR1 needs to be prioritized than other intra-frequency gap-needed measurement and all inter-freq/inter-RAT measurement.
  In FR1-FR2 NR-NR DC, NR intra-frequency gap-based measurement corresponding to NR serving carrier(s) of MCG (i.e., FR1 CCs) needs to be prioritized than other intra-frequency gap-needed measurement and all inter-freq/inter-RAT measurement.

## Slide 4
Way Forward
RAN4 further study the gap sharing for measurement prioritization problem for EN-DC in Rel-15, i.e operator’s request to enable LTE inter-frequency measurement prioritization (for inter-freq HO).
In Rel-15 late drop, RAN4 study and define the gap sharing mechanism with measurement prioritization which can be applied to NE-DC and FR1-FR2 NR-NR DC:
  The following table can be regarded as one option for the gap sharing scheme for FR1-FR2 NR-NR DC:
  Other options for FR1-FR2 NR-NR DC are not precluded.
  FFS gap sharing scheme for NE-DC in Rel-15 late drop.
  Requirements shall be completed accordingly, by allocating colliding measurement gap occasions between the two groups of carriers based on the defined gap sharing scheme.
  How to allocate measurement gap occasions within each group depends on the separate CSF discussion.
MeasGapSharingScheme | Value of X (%)
‘00’ | Equal splitting
‘01’ | [25]% MG for intra-frequency gap-based measurement corresponding to severing carrier(s) of MCG (in FR1) The rest MG for other measurement
‘10’ | [50]% MG for intra-frequency gap-based measurement corresponding to severing carrier(s) of MCG (in FR1) The rest MG for other measurement
‘11’ | [75]% MG for intra-frequency gap-based measurement corresponding to severing carrier(s) of MCG (in FR1) The rest MG for other measurement