## Slide 1: MU and TT for FR1 and FR2 Tx/Rx TRP spurious emissions
Huawei
3GPP TSG-RAN WG4 Meeting #88
Gothenburg, Sweden, 20th – 24th Aug 2018
R4-1811889

## Slide 2: FR1

## Slide 3: FR1 - Tx mandatory emissions - agreements
Currently 2 ranges
  30 MHz ≤ f ≤ 4 GHz
  4 GHz < f ≤ 19 GHz
The frequency breakpoint is at 4GHz, as we now have wanted frequency bands up to 6GHz up to 6GHz can be considered in-band in some cases so would be expected to have better MU, it is proposed to change the freq breakpoint to 6GHz as follows:
  30 MHz ≤ f ≤ 6 GHz
  6 GHz < f ≤ 19 GHz

## Slide 4: FR1 - Tx mandatory emissions - agreements
Wide band chamber analysis, new contributors are:
  Conducted measurement uncertainty – Measurement uncertainty of the RF measurement equipment and the associated RF measurement system including filters, attenuators, limiters etc… as necessary for the appropriate test
  Measurement antenna variation
  FSPL estimation error
  Uncertainty of the absolute gain of the reference antenna
SE is added RSS at 2σ
Proposal
  30 MHz ≤ f ≤ 6 GHz, MU=2.3dB
  6 GHz < f ≤ 19 GHz, MU=4.2dB
UID | Uncertainty source | Uncertainty value |  | Distribution of the probability | Divisor based on distribution shape | ci | Standard uncertainty ui [dB] | 
 |  | 30MHz<f≤6 GHz | 6GHz<f ≤19GHz |  |  |  | 30MHz<f≤6 GHz | 6GHz<f ≤19GHz
Stage 2: DUT measurement |  |  |  |  |  |  |  | 
1 | Positioning misalignment between the AAS BS and the reference antenna | 0.03 | 0.03 | Rectangular | √3 | 1 | 0.02 | 0.02
2 | Pointing misalignment between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
3 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
4 | Polarization mismatch between the AAS BS and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
5 | Mutual coupling between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
6 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
7 | Conducted measurement uncertainty | 1.02 | 2.04 | Gaussian | 1 | 1 | 1.02 | 2.04
8 | Impedance mismatch in the receiving chain | 0.2 | 0.45 | U-shaped | √2 | 1 | 0.14 | 0.32
9 | Random uncertainty | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | Measurement antenna frequency variation | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | FSPL estimation error | 0 | 0 | Gaussian | 1 | 1 | 0 | 0
 | Test system frequency flatness | 0.2 | 0.2 | Gaussian | 1 | 1 | 0.2 | 0.2
Stage 1: Calibration measurement |  |  |  |  |  |  |  | 
10 | Impedance mismatch between the receiving antenna and the network analyzer | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
11 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
12 | Impedance mismatch between the reference antenna and the network analyzer. | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
13 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
14 | Polarization mismatch for reference antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
15 | Mutual coupling between the reference antenna and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
16 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
17 | Uncertainty of the network analyzer | 0.13 | 0.2 | Gaussian | 1 | 1 | 0.13 | 0.2
18 | Influence of the reference antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
19 | Reference antenna feed cable loss measurement uncertainty | 0.06 | 0.06 | Gaussian | 1 | 1 | 0.06 | 0.06
20 | Influence of the receiving antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
21 | Uncertainty of the absolute gain of the reference antenna | 0.5 | 0.5 | Rectangular | √3 | 1 | 0.29 | 0.29
22 | Uncertainty of the absolute gain of the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  |  | 1.11 | 2.11
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  |  | 2.18 | 4.13
 | SE |  |  |  |  |  | 0.75 | 0.75
 | MU total |  |  |  |  |  | 2.3 | 4.2

## Slide 5: FR1 - Rx emissions
As with Tx the frequency breakpoint is changed to 6GHz:
  30 MHz ≤ f ≤ 6 GHz
  6 GHz < f ≤ 19 GHz
The receiver requirements are at a much lower power level so TRP calculation may be affected by the noise floor of the measurement system, the following definition is proposed:
Measurement system dynamic range uncertainty – uncertainty due to the test requirement being close to the measurement equipment noise floor and the noise floor contributing significantly to the TRP total.

## Slide 6: FR1 - Rx emissions
Same contributors as Tx SE with addition of :
  Measurement system dynamic range uncertainty
SE is added RSS at 2σ
Proposal
  30 MHz ≤ f ≤ 6 GHz, MU=2.5dB
  6 GHz < f ≤ 19 GHz, MU=4.2dB
UID | Uncertainty source | Uncertainty value |  | Distribution of the probability | Divisor based on distribution shape | ci | Standard uncertainty ui [dB] | 
 |  | 30MHz<f≤4 GHz | 4GHz<f ≤19GHz |  |  |  | 30MHz<f≤4 GHz | 4GHz<f ≤19GHz
Stage 2: DUT measurement |  |  |  |  |  |  |  | 
1 | Positioning misalignment between the AAS BS and the reference antenna | 0.03 | 0.03 | Rectangular | √3 | 1 | 0.02 | 0.02
2 | Pointing misalignment between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
3 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
4 | Polarization mismatch between the AAS BS and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
5 | Mutual coupling between the AAS BS and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
6 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
7 | Conducted measurement uncertainty (minus missmatch) | 1 | 1.99 | Gaussian | 1 | 1 | 1 | 1.99
8 | Impedance mismatch in the receiving chain | 0.2 | 0.45 | U-shaped | √2 | 1 | 0.14 | 0.32
9 | Random uncertainty | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | Measurement antenan frequency variation | 0.1 | 0.1 | Rectangular | √3 | 1 | 0.06 | 0.06
 | FSPL estimation error | 0 | 0 | Gaussian | 1 | 1 | 0 | 0
 | Measurement system dynamic range uncertainty | 0.51 | 0.51 | Gaussian | 1 | 1 | 0.51 | 0.51
 | Test system frequency flatness | 0.2 | 0.2 | Gaussian | 1 | 1 | 0.2 | 0.2
Stage 1: Calibration measurement |  |  |  |  |  |  |  | 
10 | Impedance mismatch between the receiving antenna and the network analyzer | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
11 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
12 | Impedance mismatch between the reference antenna and the network analyzer. | 0.05 | 0.05 | U-shaped | √2 | 1 | 0.04 | 0.04
13 | Quality of quiet zone | 0.1 | 0.1 | Gaussian | 1 | 1 | 0.1 | 0.1
14 | Polarization mismatch for reference antenna | 0.01 | 0.01 | Rectangular | √3 | 1 | 0.01 | 0.01
15 | Mutual coupling between the reference antenna and the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
16 | Phase curvature | 0.05 | 0.05 | Gaussian | 1 | 1 | 0.05 | 0.05
17 | Uncertainty of the network analyzer | 0.13 | 0.2 | Gaussian | 1 | 1 | 0.13 | 0.2
18 | Influence of the reference antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
19 | Reference antenna feed cable loss measurement uncertainty | 0.06 | 0.06 | Gaussian | 1 | 1 | 0.06 | 0.06
20 | Influence of the receiving antenna feed cable | 0.05 | 0.05 | Rectangular | √3 | 1 | 0.03 | 0.03
21 | Uncertainty of the absolute gain of the reference antenna | 0.5 | 0.5 | Rectangular | √3 | 1 | 0.29 | 0.29
22 | Uncertainty of the absolute gain of the receiving antenna | 0 | 0 | Rectangular | √3 | 1 | 0 | 0
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  |  | 1.21 | 2.13
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  |  | 2.37 | 4.17
 | SE |  |  |  |  |  | 0.75 | 0.75
 | MU total |  |  |  |  |  | 2.5 | 4.2

## Slide 7: FR1 - Additional requirements- co-existence
As with all the co-existence bands are 3GPP the MU’s are split in freq like the wanted signal – this can be kept.
The co-existence requirements (like the Rx emissions) are at a much lower power level so TRP calculation may be affected by the noise floor of the measurement system, the following definition is proposed:
Measurement system dynamic range uncertainty – uncertainty due to the test requirement being close to the measurement equipment noise floor and the noise floor contributing significantly to the TRP total.
Conducted MU are given for above and below -60dBm, the requirement levels are above -60dBm but the measured power for OTA will be less than -60dBm. As some contributions are lower than the conducted MU to keep the MU down the above -60dBm conducted values are used.

## Slide 8: FR1 - Additional requirements- co-existence
Bvased on CATR as this is worst case for EIRP measurement (other can be sdone bit will be lower MU).
Measurement system dynamic range uncertainty added as low power level
SE added at 2σ
Proposal
  f ≤ 3 GHz, MU=2.6dB
  3 GHz < f ≤ 4.2 GHz, MU=2.6dB
    4.2 GHz < f ≤ 6 GHz, MU=3.0dB
UID | Uncertainty source | Uncertainty value |  |  | Distribution of the probability | Divisor based on distribution shape | ci | Standard uncertainty ui [dB] |  | 
 |  | f≤3 GHz | 3GHz<f ≤4.2GHz | 4.2GHz<f ≤6GHz |  |  |  | f≤3 GHz | 3GHz<f ≤4.2GHz | 4.2GHz<f ≤6GHz
Stage 2: DUT measurement |  |  |  |  |  |  |  |  |  | 
1 | Misalignment DUT & pointing error | 0 | 0 | 0 | Exp. normal | 2 | 1 | 0 | 0 | 0
2 | Conducted measurement uncertainty (minus missmatch) | 1.02 | 1.02 | 1.28 | Gaussian | 1 | 1 | 1.02 | 1.02 | 1.28
3 | Standing wave between DUT and test range antenna | 0.21 | 0.21 | 0.21 | U-shaped | √2 | 1 | 0.15 | 0.15 | 0.15
4 | RF leakage, test range antenna cable connector terminated. | 0.0012 | 0.0012 | 0.0012 | Normal | 1 | 1 | 0.0012 | 0.0012 | 0.0012
5 | QZ ripple with DUT | 0.0928 | 0.0928 | 0.0928 | Normal | 1 | 1 | 0.0928 | 0.0928 | 0.0928
 | Measurement system dynamic range uncertainty | 0.51 | 0.51 | 0.51 | Gaussian | 1 | 1 | 0.51 | 0.51 | 0.51
 | Test system frequency flatness | 0.2 | 0.2 | Gaussian | 1 | 1 | 0.2 | 0.2 |  | 
Stage 1: Calibration measurement |  |  |  |  |  |  |  |  |  | 
6 | Network Analyzer | 0.13 | 0.2 | 0.2 | Normal | 1 | 1 | 0.13 | 0.2 | 0.2
7 | Uncertainty of return loss (S11) measurement of SGH and test receiver (VNA) ports | 0.127 | 0.325 | 0.325 | U-shaped | √2 | 1 | 0.09 | 0.23 | 0.23
8 | Insertion loss variation in receiver chain | 0.18 | 0.18 | 0.18 | Rectangular | √3 | 1 | 0.1 | 0.1 | 0.1
9 | RF leakage, test range antenna cable connector terminated. | 0.0012 | 0.0012 | 0.0012 | Normal | 1 | 1 | 0.0012 | 0.0012 | 0.0012
10 | Influence of the calibration antenna feed cable | 0.022 | 0.022 | 0.022 | U-shaped | √2 | 1 | 0.015 | 0.015 | 0.015
11 | SGH Calibration uncertainty | 0.5 | 0.433 | 0.433 | Rectangular | √3 | 1 | 0.29 | 0.25 | 0.25
12 | Misalignment positioning system | 0 | 0 | 0 | Exp. normal | 2 | 1 | 0 | 0 | 0
13 | Misalignment SGH and pointing error | 0.5 | 0.5 | 0.5 | Exp. normal | 2 | 1 | 0.25 | 0.25 | 0.25
14 | Rotary joints | 0.048 | 0.048 | 0.048 | U-shaped | √2 | 1 | 0.034 | 0.034 | 0.034
15 | Standing wave between SGH and test range antenna | 0.09 | 0.09 | 0.09 | U-shaped | √2 | 1 | 0.06 | 0.06 | 0.06
16 | QZ ripple with SGH | 0.009 | 0.009 | 0.009 | Normal | 1 | 1 | 0.009 | 0.009 | 0.009
17 | Switching uncertainty | 0.26 | 0.26 | 0.26 | Rectangular | √3 | 1 | 0.15 | 0.15 | 0.15
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  |  |  | 1.26 | 1.26 | 1.47
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  |  |  | 2.47 | 2.47 | 2.89

## Slide 9: FR1 - FR1 - TT values
The MU values have been agreed in R4-1811672
TX mandatory emissions (CAT A/B)
  TT=0
Receiver spurious emissions
  TT=MU
Additional requirements- co-existence
  For 3GPP to 3GPP co-existence, TT=MU
    Tables 6.6.5.2.3-1, 6.6.5.2.3-3, 6.6.5.2.3-4
  For PHS, TT=0
    Tables 6.6.5.2.3-2

## Slide 10: FR2

## Slide 11: FR2 – SE 30MHz to 60GHz
Based on the agreements for FR2 in-band MU and the findings in R4-1810518 , we have the following, per point MU estimations:
FR assumes a 1.2dB SE (2σ)
6 GHz to 12.75GHz is higher MU for than for FR2 in-band region.
As FR1 BS is physically larger, there are larger errors at higher frequenies so the FR2 in-band MU is assumed in this region.
 | 30 MHz < f ≦ 380 MHz | 380 MHz < f ≦ 1.7 GHz | 1.7 GHz < f ≦ 3 GHz | 3 GHz < f ≦ 3.8 GHz | 3.8 GHz < f ≦ 6GHz | 6 GHz < f ≦ 12.75 GHz | 12.75 GHz < f ≦ 18 GHz |  | 18 GHz < f ≦ 26.5 GHz | 26.5 GHz < f ≦ 40 GHz | 40 GHz < f ≦ 60 GHz
IAC (paper) | 1.87 | 1.87 |  | 1.96 | 2.15 |  | 2.18 |  |  |  | 
IAC (numbers) | 1.20 | 1.20 |  | 1.37 | 1.61 |  | 1.61 |  | 2.40 | 2.67 | 5.03
CATR |  |  | 1.56 | 1.67 | 1.68 |  | 1.75 |  | 2.34 | 2.35 | 5.03
MU | 1.87 | 1.87 | 1.87 | 1.96 | 2.15 |  | 2.18 |  | 2.4 | 2.7 | 5.0
FR1 (for information) | 2.30 |  |  |  |  | 4.20 |  |  |  |  | 
FR2 in-band (for information) |  |  |  |  |  |  |  |  | 2.7 | 2.7 | 
 | 30 MHz < f ≦ 6 GHz |  |  |  |  | 6 GHz < f ≦ 18 GHz |  |  | 18 GHz < f ≦ 26.5 GHz | 26.5 GHz < f ≦ 40 GHz | 40 GHz < f ≦ 60 GHz
Agreement | 2.3 |  |  |  |  | 2.7 |  |  | 2.7 | 2.7 | 5
 | From FR1 |  |  |  |  | same as FR2 in-band |  |  | FR2 in-band |  | oob

## Slide 12: FR2 – SE 40GHz to 60GHz – MU Budgets
Compact Antenna Test Range uncertainty assessment for FR2 OTA transmitter spurious emissions measurement 18GHz – 60 GHz |  |  |  |  |  | 
UID | Uncertainty source |  | Distribution of the probability | Divisor based on distribution shape | ci | 
 |  | 40 GHz < f ≦ 60 GHz |  |  |  | 40 GHz < f ≦ 60 GHz
Stage 2: DUT measurement |  |  |  |  |  | 
1 | Misalignment DUT & pointing error | 0.3 | Rectangular | √3 | 1 | 0.173
2 | RF power measurement equipment (e.g. spectrum analyzer, power meter) | 0.7 | Gaussian | 1 | 1 | 0.7
21 | Uncertainty of the LNA | 0 | Gaussian | 1 | 1 | 0
22 | Uncertainty of the Mixer | 2.25 | Gaussian | 1 | 1 | 2.25
3 | Standing wave between DUT and test range antenna | 0.21 | U-shaped | √2 | 1 | 0.148
4 | RF leakage, test range antenna cable connector terminated. | 0.001 | Normal | 1 | 1 | 0.001
5 | QZ ripple with DUT | 0.0928 | Normal | 1 | 1 | 0.0928
 | test system frequency flatness | 0.25 | Gaussian | 1 | 1 | 0.25
19 | Miscellaneous uncertainty | 0 | Rectangular | √3 | 1 | 0.000
Stage 1: Calibration measurement |  |  |  |  |  | 
6 | Network Analyzer | 0.3 | Normal | 1 | 1 | 0.3
7 | Uncertainty of return loss (S11) measurement of SGH and test receiver (VNA) ports | 0.57 | U-shaped | √2 | 1 | 0.403
8 | Insertion loss variation in receiver chain | 0.18 | Rectangular | √3 | 1 | 0.104
9 | RF leakage, test range antenna cable connector terminated. | 0.001 | Normal | 1 | 1 | 0.001
10 | Influence of the calibration antenna feed cable | 0.29 | U-shaped | √2 | 1 | 0.205
11 | SGH Calibration uncertainty | 0.52 | Rectangular | √3 | 1 | 0.300
12 | Misalignment positioning system | 0 | Exp. normal | 2 | 1 | 0
13 | Misalignment SGH and pointing error | 0.5 | Exp. normal | 2 | 1 | 0.25
14 | Rotary joints | 0 | U-shaped | √2 | 1 | 0.000
15 | Standing wave between SGH and test range antenna | 0.09 | U-shaped | √2 | 1 | 0.064
16 | QZ ripple with SGH | 0.009 | Normal | 1 | 1 | 0.009
17 | Switching uncertainty | 0.43 | Rectangular | √3 | 1 | 0.248
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  | 2.5
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  | 4.9
 |  |  |  |  | SE | 1.2
 |  |  |  |  | total | 5.03
Indoor Anechoic Chamber uncertainty assessment for FR2 OTA transmitter spurious emissions measurement 40 GHz – 60GHz |  |  |  |  |  | 
UID | Uncertainty source |  | Distribution of the probability | Divisor based on distribution shape | ci | 
 |  | 40 GHz < f ≦ 60 GHz |  |  |  | 40 GHz < f ≦ 60 GHz
Stage 2: DUT measurement |  |  |  |  |  | 
1 | Positioning misalignment between the AAS BS and the reference antenna | 0.018 | Rectangular | √3 | 1 | 0.010
2 | Pointing misalignment between the AAS BS and the receiving antenna | 0 | Rectangular | √3 | 1 | 0.000
3 | Quality of quiet zone | 0.1 | Gaussian | 1 | 1 | 0.100
4 | Polarization mismatch between the AAS BS and the receiving antenna | 0.018 | Rectangular | √3 | 1 | 0.010
5 | Mutual coupling between the AAS BS and the receiving antenna | 0 | Rectangular | √3 | 1 | 0.000
6 | Phase curvature | 0.05 | Gaussian | 1 | 1 | 0.050
7 | Uncertainty of the RF Power Measurement Equipment | 0.6 | Gaussian | 1 | 1 | 0.600
 | test system frequency flatness | 0.25 | Gaussian | 1 | 1 | 0.25
23 | Uncertainty of the LNA | 0 | Gaussian | 1 | 1 | 0.000
24 | Uncertainty of the Mixer | 2.25 | Gaussian | 1 | 1 | 2.250
8 | Impedance mismatch in the receiving chain | 0.42 | U-shaped | √2 | 1 | 0.297
9 | Random uncertainty | 0.1 | Rectangular | √3 | 1 | 0.058
Stage 1: Calibration measurement |  |  |  |  |  | 
10 | Impedance mismatch between the receiving antenna and the network analyzer | 0.57 | U-shaped | √2 | 1 | 0.403
11 | Positioning and pointing misalignment between the reference antenna and the receiving antenna | 0.43 | Rectangular | √3 | 1 | 0.248
12 | Impedance mismatch between the reference antenna and the network analyzer. | 0.57 | U-shaped | √2 | 1 | 0.403
13 | Quality of quiet zone | 0.1 | Gaussian | 1 | 1 | 0.100
14 | Polarization mismatch for reference antenna | 0.018 | Rectangular | √3 | 1 | 0.010
15 | Mutual coupling between the reference antenna and the receiving antenna | 0 | Rectangular | √3 | 1 | 0.000
16 | Phase curvature | 0.07 | Gaussian | 1 | 1 | 0.070
17 | Uncertainty of the network analyzer | 0.3 | Gaussian | 1 | 1 | 0.300
18 | Influence of the reference antenna feed cable | 0.18 | Rectangular | √3 | 1 | 0.104
19 | Reference antenna feed cable loss measurement uncertainty | 0.1 | Gaussian | 1 | 1 | 0.100
20 | Influence of the receiving antenna feed cable | 0.18 | Rectangular | √3 | 1 | 0.104
21 | Uncertainty of the absolute gain of the reference antenna | 0.52 | Rectangular | √3 | 1 | 0.300
22 | Uncertainty of the absolute gain of the receiving antenna | 0 | Rectangular | √3 | 1 | 0.000
Combined standard uncertainty (1σ) [dB] |  |  |  |  |  | 2.49
Expanded uncertainty (1.96σ - confidence interval of 95 %) [dB] |  |  |  |  |  | 4.88
 |  |  |  |  | SE | 1.2
 |  |  |  |  | total | 5.03

## Slide 13: FR2 – TX SE 30MHz to 60GHz
The following MU’s are proposed
  30 MHz < f ≤ 6 GHz, MU=2.3 dB
    (same as FR1)
    6 GHz < f ≤ 18 GHz, MU=2.7 dB
      (same as FR2 in-band)
    18 GHz < f ≤ 40 GHz, MU=2.7 dB
      (FR2 in-band region)
    40 GHz < f ≤ 60 GHz, MU=5.0 dB
      (larger value as mixer needed)

## Slide 14: FR2 – RX SE 30MHz to 60GHz
The following MU’s are proposed
  30 MHz ≤ f ≤ 6 GHz, MU=2.5dB
    Same as FR1 RX
    6 GHz < f ≤ 18 GHz, MU=2.7 dB
      (same as FR2 in-band Tx)
    18 GHz < f ≤ 40 GHz, MU=2.7 dB
      (same as FR2 Tx)
    40 GHz < f ≤ 60 GHz, MU=5.0 dB
      (same as FR2 Tx)

## Slide 15: FR2 - TT values
TX mandatory emissions (CAT A/B)
  TT=0
Receiver spurious emissions
  30MHz to 12.75GHz, TT=MU
    As per FR1 for the same reason
  12.75GHz to 80MHz (top freq currently considered fro MU), TT=0
    As requirement is higher (same as CAT B)
There are currently no Additional requirements for FR2