## Slide 1: Way forward on specifying NR demodulation
Anritsu, Rohde & Schwarz, Keysight, Spirent,
Qualcomm, Intel
3GPP TSG-RAN WG4 Meeting#88
Gothenburg, Sweden, 20–24 August, 2018
R4-1811892

## Slide 2: Requirements to be specified in TS 38.101-4
Absolute Noc level. at Reference point, for bands up to 40GHz
  Noc level may have different value according to UE type
SNR at Reference point SNRRP, test-specific value
Downlink signal and noise aligned to the Rx beam peak
How to capture the methodology in 38.101-4 is FFS in NR UE Demodulation session
  FFS whether to include the relation between Baseband SNR and SNR at reference point in 38.101-4 and is up to further discussion

## Slide 3: Reference point SNR and Baseband SNR
Principle of calculation:
  Set wanted noise to give 1dB difference between Reference point SNR and Baseband SNR, using agreed UE parameters
  SNRRP = SNRBB + 1dB

## Slide 4: Assumptions on UE parameters
Values derived from UE assumptions for EIS defined in R4-1804589, 39GHz
  These parameters together with 1dB difference between Reference point SNR and Baseband SNR, give Noc level of -153dBm/Hz at Reference point
  The Noc value can be changed for other device types/categories in Rel-15 or future releases, maintaining SNRRP = SNRBB + 1dB

## Slide 5: Maximum feasible SNR level
Values derived from Test system assumptions agreed by TE vendors
  These are UE baseband SNR values. Figures used in TS 38.101-4 will be 1dB higher
  Values based on UE parameters and currently foreseen test equipment limitations as derived in R4-1809772, and could be improved in future