## Slide 1: Way forward on sTTI BS demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 – 12 October, 2018
R4-1813708

## Slide 2: Introduction
RAN4#88 collected the PUSCH and SPUCCH simulation results [1].
It is observed the large span for some test cases for SPUCCH format 4.
This way forward propose how to derive the final BS demodulation requirements for sTTI.

## Slide 3: Requirements for PUSCH
Set the requirement by adding 2.5dB margin on top of the average of alignment results. Note the values in (AVE+2.5) have been set in TS36.101 15.4.0 in square brackets.
Rx antennas | CBW | Ericsson | Huawei | Nokia | Samsung | STD | SPAN | AVE | AVE+2.5
2Rx | 5MHz | 8.8 | 9.3 | 10.3 | 10.3 | 0.7 | 1.5 | 9.7 | 12.2
 | 10MHz | 8.8 | 9.31 | 10.4 | 10.2 | 0.7 | 1.6 | 9.7 | 12.2
 | 15MHz | 8.8 | 9.3 | 10.5 | 10.2 | 0.8 | 1.7 | 9.7 | 12.2
 | 20MHz | 9.1 | 9.3 | 10.8 | 10.5 | 0.8 | 1.7 | 9.9 | 12.4
4Rx | 5MHz | 6.1 | 6.32 | 6.7 | 6.4 | 0.3 | 0.7 | 6.4 | 8.9
 | 10MHz | 6.0 | 6.31 | 6.7 | 6.5 | 0.3 | 0.6 | 6.4 | 8.9
 | 15MHz | 5.9 | 6.31 | 6.7 | 6.4 | 0.3 | 0.8 | 6.3 | 8.8
 | 20MHz | 6.6 | 6.31 | 7.0 | 6.7 | 0.3 | 0.7 | 6.6 | 9.1

## Slide 4: Requirements for SPUCCH format 1a
Set the requirement by adding 2.5dB margin on top of the average of alignment results. Note the values in (AVE+2.5) have been set in TS36.101 15.4.0 in square brackets.
Rx antennas | CBW | Ericsson | Huawei | Nokia | Samsung | STD | SPAN | AVE | AVE+2.5
2Rx | 5MHz | 0.1 | 1.8 | 1.6 | 1.5 | 0.7 | 1.6 | 1.2 | 3.7
 | 10MHz | 0.3 | 1.8 | 1.7 | 0.9 | 0.7 | 1.5 | 1.1 | 3.6
 | 15MHz | 0.3 | 2.3 | 1.4 | 1.1 | 0.8 | 2.0 | 1.3 | 3.8
 | 20MHz | 0.3 | 2.3 | 1.4 | 1.1 | 0.8 | 2.0 | 1.3 | 3.8
4Rx | 5MHz | -3.9 | -1.6 | -2.3 | -2.8 | 0.9 | 2.2 | -2.6 | -0.1
 | 10MHz | -3.8 | -1.5 | -2.3 | -3.0 | 1.0 | 2.3 | -2.7 | -0.2
 | 15MHz | -3.7 | -1.3 | -2.3 | -3.1 | 1.1 | 2.5 | -2.6 | -0.1
 | 20MHz | -3.8 | -1.4 | -2.4 | -3.0 | 1.0 | 2.4 | -2.6 | -0.1

## Slide 5: Proposed requirements for SPUCCH format 4
Set the requirement by adding 2.5dB margin on top of the average of alignment results.
Rx antennas | CBW | Ericsson | Huawei | Nokia | Samsung | STD | SPAN | AVE | AVE+2.5
2Rx | 5MHz |  | 4.3 | 4.7 | 2.1 | 1.1 | 2.6 | 3.7 | 6.2
 | 10MHz |  | 4.6 | 4.9 | 2.0 | 1.6 | 2.9 | 3.8 | 6.3
 | 15MHz |  | 4.3 | 4.8 | 1.9 | 1.5 | 2.9 | 3.7 | 6.2
 | 20MHz |  | 4.5 | 4.9 | 1.8 | 1.7 | 3.1 | 3.7 | 6.2
4Rx | 5MHz |  | -0.6 | -1.1 | -4.3 | 2.0 | 3.7 | -2.0 | 0.5
 | 10MHz |  | -0.5 | -1.1 | -4.3 | 2.0 | 3.8 | -2.0 | 0.5
 | 15MHz |  | -0.3 | -1.1 | -4.0 | 1.9 | 3.7 | -1.8 | 0.7
 | 20MHz |  | -0.2 | -1.0 | -4.0 | 2.0 | 3.8 | -1.7 | 0.8

## Slide 6: References
R4-1811240, “Summary results for sTTI sPUSCH and sPUCCH”, Ericsson.