## Slide 1: Scaling factor for measurement objects with multiple frequencies
Mediatek
3GPP TSG-RAN WG4 RAN#88 Bis
Chengdu, China, 8th- 12th October, 2018
R4-1813713
Document for: Approval

## Slide 2: Background
Agreed 5 scenarios for intra-frequency measurement without gap (agreed in #AH1807 meeting [1])
RAN4 to specify the requirements of following 5 scenarios:
Scenario A: 1a/1b. Fully overlapped between MG and SMTC in Type A/B
Scenario B1: 2a/2b. Partial overlapped between MG and SMTC in Type A/B.
  The SMTC in Type A/B and RLM-RS are partially overlapped
Scenario B2: 2a/2b. Partial overlapped between MG and SMTC in Type A/B.
  The SMTC in Type A/B and RLM-RS are fully overlapped
Scenario C1: 3a/3b. Fully non-overlapped between MG and SMTC in Type A/B.
  The SMTC in Type A/B and RLM-RS are partially overlapped
Scenario C2: 3a/3b. Fully non-overlapped between MG and SMTC in Type A/B.
  The SMTC in Type A/B and RLM-RS are fully overlapped
  It is noted that Type A/B/C/D should be also clarified in the spec

## Slide 3: Background
Requirements assuming UE conducts measurement outside measurement gap
  Intra-frequency measurement without gap with partial overlapped between MG and SMTC
    Type A/B measurement under scenarios B1/B2
  Intra-frequency measurement without gap with Fully non-overlapped between MG and SMTC in Type A/B
    Type A/B measurement under scenarios C1/C2
Requirements assuming UE conducts measurement within measurement gap
  Intra-frequency measurement without gap with fully overlapped between MG and SMTC
    Type A/B measurement under scenarios A
  Intra-frequency measurement with gap
    Type C
  Inter-frequency measurement
    Type D
  Inter-RAT measurement
    Type D

## Slide 4: Background: Current spec structure
Chapters in spec | Requirements | Scaling factor | Comments
9.1 general measurement requirement |  |  | N.A
9.2 Intra-frequency measurement |  |  | N.A
9.2.5 Intra-frequency measurement with no measurement gap (Type A/B) | Fully overlapped between MG and SMTC | Kca | Measurement within gap only [Scenario A]
 | Partial overlapped between MG and SMTC |  | Measurement outside gap only [Scenario B1,B2]
 | Fully non-overlapped between MG and SMTC |  | Measurement outside gap only [Scenario C1,C2]
9.2.6 Intra-frequency measurement with measurement gap (Type C) |  | N/A | Measurement within gap only
9.3 NR inter-frequency measurement (Type D) |  | CSFinter | Measurement within gap only
9.4 NR inter-RAT measurement (Type D) |  | K | Measurement within gap only

## Slide 5
Chapters in spec | Requirements | Value of scaling factor | Comments
9.1 general measurement requirement |  |  | N.A
9.1.5 carrier specific scaling factor |  |  | 
9.1.5.1 monitoring of multiple layers outside gap | for NSA and SA |  | Type A/B in scenario B1, B2, C1, C2
9.1.5.2 monitoring of multiple layers within gap | for NSA and SA |  | Type A/B in scenario A Type C and D
9.2 Intra-frequency measurement |  |  | N.A
9.2.5 Intra-frequency measurement with no measurement gap (Type A/B) | Fully overlapped between MG and SMTC | Kca refer to [9.1.5.2] | Measurement within gap only [Scenario A]
 | Partial overlapped between MG and SMTC | Kca refer to [9.1.5.1] | Measurement outside gap only [Scenario B1,B2]
 | Fully non-overlapped between MG and SMTC | Kca refer to [9.1.5.1] | Measurement outside gap only [Scenario C1,C2]
9.2.6 Intra-frequency measurement with measurement gap (Type C) |  | N/A refer to [9.1.5.2] | Measurement within gap only
9.3 NR inter-frequency measurement (Type D) |  | CSFinter refer to [9.1.5.2] | Measurement within gap only
9.4 NR inter-RAT measurement (Type D) |  | K refer to [9.1.5.2] | Measurement within gap only
Wayforward: Suggested new spec structure

## Slide 6: Wayforward: Re-naming in section 9.2, 9.3, and 9.4
Chapters in spec | Parameters used in requirement | Value taken from
9.2.5 Intra-frequency measurement with no measurement gap | Kca becomes CSSFintra | [9.1.5.2] under fully overlapped between MG and SMTC
 |  | [9.1.5.1] under partial overlapped between MG and SMTC
 |  | [9.1.5.1] under fully non-overlapped between MG and SMTC
9.2.6 Intra-frequency measurement with measurement gap | Add CSSFintra | [9.1.5.2]
9.3 NR inter-frequency measurement | CSFinter becomes CSSFinter | [9.1.5.2]
9.4 NR inter-RAT measurement | K becomes CSSFinterRAT | [9.1.5.2]

## Slide 7: Wayforward: Naming in section 9.1.5
Chapters in spec | Requirements | Value of scaling factor | Comments
9.1 general measurement requirement |  |  | N.A
9.1.5 carrier specific scaling factor |  |  | 
9.1.5.1 monitoring of multiple layers outside gap | for NSA and SA Naming rule? |  | Type A/B in scenario B1, B2, C1, C2
9.1.5.2 monitoring of multiple layers within gap | for NSA and SA Naming rule? |  | Type A/B in scenario A Type C and D
Options for naming in 9.1.5:
  Option 1:
    9.1.5.1 : CSSFoutside_gap_i
    9.1.5.2 : CSSFwithin_gap_i
  Option 2:
    9.1.5.1 : CSSFintra_outside_gap_i
    9.1.5.2 : CSSFinter_i and CSSFintra_within_gap_i

## Slide 8: 9.2.5 Intra-frequency measurement with no measurement gap
      Fully overlapped between MG and SMTC,
        PSS/SSS detection in FR1 under DRX<=320ms as an example
        CSSFintra euqals CSSFwithin_gap_i (option1) or CSSFintra_within_gap_i (option2)
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 

## Slide 9: 9.2.5 Intra-frequency measurement with no measurement gap
      Partial overlapped between MG and SMTC.
        The SMTC in Type A/B and RLM-RS are partially overlapped
        PSS/SSS detection in FR1 under DRX<=320ms as an example
        CSSFintra euqals CSSFoutside_gap_i (option1) or CSSFintra_outside_gap_i (option2)
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 

## Slide 10: 9.2.5 Intra-frequency measurement with no measurement gap
      Partial overlapped between MG and SMTC.
        The SMTC in Type A/B and RLM-RS are fully overlapped
        PSS/SSS detection in FR2 under DRX<=320ms as an example
        CSSFintra euqals CSSFoutside_gap_i (option1) or CSSFintra_outside_gap_i (option2)
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 

## Slide 11: 9.2.5 Intra-frequency measurement with no measurement gap
      Fully non-overlapped between MG and SMTC.
        The SMTC in Type A/B and RLM-RS are partially overlapped
        PSS/SSS detection in FR1 under DRX<=320ms as an example
        CSSFintra euqals CSSFoutside_gap_i (option1) or CSSFintra_outside_gap_i (option2)
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 

## Slide 12: 9.2.5 Intra-frequency measurement with no measurement gap
      Fully non-overlapped between MG and SMTC.
        The SMTC in Type A/B and RLM-RS are fully overlapped
        PSS/SSS detection in FR2 under DRX<=320ms as an example
        CSSFintra euqals CSSFoutside_gap_i (option1) or CSSFintra_outside_gap_i (option2)
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 
Type A/B | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 

## Slide 13: 9.2.6 Intra-frequency measurement with measurement gap
        PSS/SSS detection in FR1 under DRX<=320ms as an example
        CSSFintra euqals CSSFwithin_gap_i (option1) or CSSFintra_within_gap_i (option2)
Type C | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 
Type C | PCell/ PSCell | 
 | activated SCells | 
 | deactivated SCells | 

## Slide 14: 9.3 NR inter-frequency measurement
        PSS/SSS detection in FR1 under DRX<=320ms as an example
        CSSFinter euqals CSSFwithin_gap_i (option1) or CSSFinter_i (option2)
Type D | NR inter freq. | 
Type D | NR inter freq. | 

## Slide 15: 9.4 NR inter-RAT measurement
 |  | Identify the E-UTRAN FDD inter-RAT cells
Type D | LTE inter -RAT | ,
 |  | Identify the E-UTRAN FDD inter-RAT cells
Type D | LTE inter -RAT | 
        CSSFinterRAT euqals CSSFwithin_gap_i (option1) or CSSFinter_i (option2)

## Slide 16: Reference
[1] R4-1809353, Discussion summary for UE measurement gap AI 5.2.3, Intel, July, 2018.