## Slide 1: 3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 08 - 12 Oct 2018
Ericsson
Way forward on simulation assumption for demodulation performance requirements for network-based CRS interference mitigation
R4-1813715

## Slide 2: WF
Define performance requirements for the UE supporting nw-BasedCRS-InterferenceMitigation-r15.
  The baseline receiver for such requirements is LMMSE-IRC
  CRS muting pattern
    Option 1: The interference cell CRS is configured with CRS muting pattern where every [two] radio frames consist of [11] subframes with full system BW CRS followed by [9] subframes with CRS only on the center 6 PRBs.
    Option 2: The interference cell CRS muting is applied in all subframes.
    One of the options above will be decided in next meeting in order to close the WI.
Define one TM3 test with 2Rx only
Simulation assumptions are listed in next page and companies are encouraged to bring alignment and impairment results for both options in next meeting.

## Slide 3: Simulation assumptions for TM3 tests
Parameter |  | Unit | Test 1 | 
 |  |  | Cell 1 | Cell 2
Downlink power allocation |  | dB | -3 | -3
 |  | dB | -3 (NOTE 1) | -3 (NOTE 1)
 |  | dB | 0 | 0
at antenna port |  | dBm/15kHz | -98 | -98
PDSCH transmission mode |  |  | 3 | NA
CRS transmission |  |  | On | . See slide 2
nw-BasedCRS-InterferenceMitigation-r15 |  |  | Disabled | Enabled
Cell ID |  |  | 0 | 1
Time offset |  |  | NA | 0
Frequency offset |  |  | NA | 0
E_s/N_oc |  |  | NA | For FRC Option 1: 10 For FRC Option 2: 5
Correlation matrix and antenna config. |  |  | 2x2 Low | 2x2 Low
Bandwidth |  |  | 10MHz | 10MHz
Channel model |  |  | [EVA5] | [EVA5]
FRC |  |  | Option 1: R.11 (FDD/TDD) Option 2: R.10 (FDD/TDD) Modify FRC such that only 41PRB are allocated and 9 center PRBs are excluded | NA
NOTE 1: . NOTE 2: Interested companies can bring results with other FRC and interference level with the purpose to identify any technical issues if there is any. |  |  |  |