## Slide 1: Way forward on measurement gap and interruption time
ZTE, Ericsson, LG
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 - 12 October, 2018
R4-1814070

## Slide 2: Background
According to interruption requirements for SA and Sync EN-DC, for 15kHz SCS serving cell(s)
  The total interruption time in current spec is 1ms longer than measurement gap length if 0.5ms MGTA is applied.
  For NR CA with 15kHz SCS carriers and 30kHz SCS carriers, the UE can not be scheduled in the half slots before and after measurement gap on 15kHz SCS carriers but can in slots before and after measurement gap on 30kHz SCS carriers which are time overlapped with half slots on 15kHz SCS carrier .

## Slide 3: Background
In LTE it would be fine to have interruption requirements with subframe granularity as the scheduling is on suframe level.
In NR, the scheduling is much more flexible
  Downlink and uplink scheduling time between control channel and data channel is configurable and allows for up to 32 slots.
  Downlink HARQ feedback time is configurable.
  Not allow using the half slots before and after measurement gap will degrade UE throughput and system performance
  Complexity on UE implementation is small.

## Slide 4: Proposed interruption requirements
  For SA and sync EN-DC, when 0.5ms MGTA is applied
    The interruption time is the same as measurement gap length, regardless of SCS of a serving cell.
    For 15kHz SCS carrier, the half slots before and after measurement gap that not overlapped with measurement gap should be allowed for scheduling.
    UE behaviour for the partially overlapped slots is FFS

## Slide 5: WF
Companies are encouraged to bring further analysis on interruption requirements for measurement gap and UE behaviour for the half slots in the RAN4#89 meeting.
Need to clarify UE behavior during interrupted half slots.