## Slide 1: WF on beam correspondence
Qualcomm, MediaTek, Sony, LGE, Verizon, Samsung, DOCOMO
3GPP TSG-RAN WG4 Meeting #88b R4-1814153
Chengdu, China, 8th – 12th October, 2018
Agenda item: 7.6.14.3

## Slide 2: Agreements
The following text is agreed for BC correspondence requirement and shall be included as a part of a draft CR to 38.101-2:
  UEs which support beam correspondence shall have the ability to select a corresponding beam for UL transmission based on DL measurements without relying on network-assisted UL beam refinement.
  For power class 3 UEs which support beam correspondence, the requirement is fulfilled if the UE’s corresponding UL beams satisfy the minimum peak EIRP according to Table 6.2.1.3-1 and spherical coverage requirements according to Table 6.2.1.3-3.

## Slide 3: Open issues to be resolved in #89
The following open issues need to be addressed in RAN4 #89:
  DL measurement signals
    If DL measurement signals need to specify in RAN4 or RAN5 specifications
    Which DL measurement signals (SSB and/or CSI-RS) should be specified
  SRS
    whether clarification on SRS configuration used in the BC test is needed in RAN4 or RAN5 specs
  A clarification on polarization of DL signals used by TE should be included in a recommendation to RAN5
Which requirement needs to be specified for PC1, PC2 and PC4

## Slide 4: References (from RAN4 #88bis)
R4-1811805, “WF on beam correspondence,” Qualcomm Incorporated.
R4-1812197, “On Beam Correspondence requirements”, Intel Corporation.
R4-1812392, “Further views on beam correspondence”, Apple Inc.
R4-1812393, “Draft CR to TS 38.101-2: Introduction of the requirement on beam correspondence”, Apple Inc.
R4-1812722, “Discussion on the polarization setting in beam correspondence and other requirements”, OPPO.
R4-1813362, “Draft CR to 38.101-2: FR2 Beam Correspondence Requirement”, Qualcomm Incorporated.
R4-1813363, “Measured Data Supporting PC3 Beam Correspondence Criterion”, Qualcomm Incorporated.
R4-1813364, “On Beam Correspondence Requirement”, Qualcomm Incorporated
R4-1813406, “Metrics for beam correspondence”, Sony, Ericsson.
R4-1813478, “On beam correspondence”, Huawei, HiSilicon.
R4-1813832, “Beam Correspondence Ad Hoc minutes”, Qualcomm Incorprated.