## Slide 1: Way Forward on Measurement Grids for Beam Peak Search & Spherical Coverage
Keysight Technologies, Rohde&Schwarz
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 – 12 October 2018 Agenda Item: 10.1.1
R4-1814310

## Slide 2: Background
Two measurement grids are considered
  Beam Peak Search Grid: using this grid, the TX and RX beam peak direction will be determined using 3D EIRP (for TX beam peak direction) and 3D RSRP/Throughput/EIS measurements (for RX beam peak directions).
  Spherical Coverage Grid: using this grid, the CDF of EIRP/EIS values in 3D is calculated to determine the spherical coverage performance.

## Slide 3: Background
TX and RX Beam Peak Search approaches currently defined in TR38.810 require a very large number of grid points which in effect yield long test times
  TX: The TX beam peak direction is found with a 3D EIRP scan (separately for each orthogonal polarization) with a grid points that is 10224 (2.5deg step size) using constant step approach or 7080 using constant density approach (using the charged particle implementation).
  RX: The RX beam peak direction is found with a 3D RSRP scan (separately for each orthogonal polarization) with a same grid points as 3D EIRP scan. The RX beam peak direction is where the maximum total component of RSRP is found.
Based on the high relative RSRP accuracy of [±6]dB, the current assumption “The RX beam peak direction is where the maximum total component of RSRP is found.” can no longer be used to determine the RX beam peak direction if the search approach is solely based on RSRP.
The minimum number of grid points and associated MU elements for EIRP/EIS spherical coverage test cases require the agreement of antenna and beamformer assumptions made this meeting in [R4-1813581 or R4-1813864]

## Slide 4: Simulation Assumptions for Spherical Coverage
Orientations/Rotations:
  10000 random relative orientations between the simulated UE and the respective measurement grids will be analysed
  The rotations of UE/grid will be along q and f as well as around the beam peak
  The rotations along q will utilize a sin(q) weighting to assume a uniform sampling on the surface
When using constant step size measurement grids, a theta-dependent correction shall be applied, i.e., the PDF probability contribution for each measurement point is scaled by sin(theta)

## Slide 5: EIRP Spherical Coverage
Using the agreed antenna & beamformer and simulation assumptions, companies are encouraged to determine the minimum number of grid points for PC3 EIRP spherical coverage test cases for MUs (at 50%-tile CDF) of 0.5, 1.0 and 1.5 dB
  The main analyses should be performed with the TX beam peak aligned on grid points
  Analyses may be performed for constant step as well as constant density grids
  Analyses for additional MUs are not precluded

## Slide 6: EIRP Spherical Coverage
Options:
MU | Constant Step Size Grid with beam peak aligned on grid points | Constant Density Grid with beam peak aligned on grid points
0.5 dB | # of Test Points: 10224 (2.5deg step size) | # of Test Points:
1.0 dB | # of Test Points: | # of Test Points:
1.5 dB |  | 

## Slide 7: TX Beam Peak Search
Test time can be reduced by relaxing the reducing the min. number of grid points while increasing the MU of the TX Beam Peak Search
A concrete proposal for TX Beam Peak Search based on a coarse search (10o constant step size) and a fine search (2.5o constant step size) was presented in [R4-1813582] which could yield savings in test time
  Note: other angular step sizes are not precluded

## Slide 8: EIRP Beam Peak Search
Options:
MU | Single Constant Step Size Grid | Single Constant Density Grid | Coarse&Fine Constant Step Size Grid | Coarse&Fine Constant Density Grid
0.5dB | 10224 (2.5deg step size) | Grid Details: # of Test Points: | Coarse Grid Details: Fine Grid Details: # of Test Points: | Coarse Grid Details: Fine Grid Details: # of Test Points:
1dB | Grid Details: # of Test Points: | Grid Details: # of Test Points: | Coarse Grid Details: Fine Grid Details: # of Test Points: | Coarse Grid Details: Fine Grid Details: # of Test Points:
1.5 dB | Grid Details: # of Test Points: | Grid Details: # of Test Points: | Coarse Grid Details: Fine Grid Details: # of Test Points: | Coarse Grid Details: Fine Grid Details: # of Test Points:

## Slide 9: EIS Spherical Coverage
Test time could be reduced by adopting an RSRQ based search as proposed in [R4-1813270]
Using the agreed antenna&beamformer and simulation assumptions, companies are encouraged to determine the minimum number of grid points for PC3 EIS spherical coverage test cases for MUs (at 50%-tile CDF) of 0.5, 1.0 and 1.5 dB
  Analyses may be performed for constant step as well as constant density grids
  Analyses for additional MUs are not precluded

## Slide 10: EIS Spherical Coverage
Options:
MU | Constant Step Size Grid with beam peak aligned on grid points with EIS sweep | Constant Density Grid with beam peak aligned on grid points with EIS sweep | Constant Step Size Grid with beam peak aligned on grid points with RSRQ search | Constant Density Grid with beam peak aligned on grid points with RSRQ search
0.5dB | # of Test Points: | # of Test Points: | # of Test Points: | # of Test Points:
1dB | # of Test Points: | # of Test Points: | # of Test Points: | # of Test Points:
1.5 dB | # of Test Points: | # of Test Points: | # of Test Points: | # of Test Points:

## Slide 11: RX Beam Peak Search
Test time can be reduced by relaxing the grid spacing of the constant step size grids while increasing the MU of the RX Beam Peak Search, e.g., as proposed in [R4-1813583], a 1dB accuracy of the RX beam peak search yields a constant step size spacing of 3.75o
  Study MUs of 0.5dB, 1dB, and 1.5dB. Analyses for additional MUs are not precluded
A concrete proposal for RX Beam Peak Search based on a coarse search (15o constant step size) based on throughput and a fine search (3.75o constant step size) based on EIS was presented in [R4-1813582] which could yield savings in test time
EIS search time can be optimized based on coarse&fine search algorithms for power levels as outlined in [R4-1812704]

## Slide 12: RX Beam Peak Search
As proposed in [R4-1813273], a coarse search based on RSRP with a subsequent EIS search could be used to reduce test time.

## Slide 13: RX Beam Peak Search
Options:
MU | Single Constant Step Size Grid | Single Constant Density Grid | Coarse&Fine Constant Step Size Grid | Coarse&Fine Constant Density Grid
0.5dB | Search Based on: Search Details: Grid Details: # of Test Points: | Search Based on: Search Details: Grid Details: # of Test Points: | Coarse Search Based on: Throughput, EIS, RSRP, etc Search Details: EIS vs RSRQ, EIS search algorithm Coarse Grid Details: Fine Grid Details: # of Test Points: | Coarse Search Based on: Throughput, EIS, RSRP, etc Search Details: EIS vs RSRQ, EIS search algorithm Coarse Grid Details: Fine Grid Details: # of Test Points:
1dB | Search Based on: Search Details: Grid Details: # of Test Points: | Search Based on: Search Details: Grid Details: # of Test Points: | Coarse Search Based on: Throughput, EIS, etc Search Details: EIS vs RSRQ, EIS search algorithm Coarse Grid Details: Fine Grid Details: # of Test Points: | Coarse Search Based on: Throughput, EIS, etc Search Details: EIS vs RSRQ, EIS search algorithm Coarse Grid Details: Fine Grid Details: # of Test Points:
1.5dB | Search Based on: Search Details: Grid Details: # of Test Points: | Search Based on: Search Details: Grid Details: # of Test Points: | Coarse Search Based on: Throughput, EIS, etc Search Details: EIS vs RSRQ, EIS search algorithm Coarse Grid Details: Fine Grid Details: # of Test Points: | Coarse Search Based on: Throughput, EIS, etc Search Details: EIS vs RSRQ, EIS search algorithm Coarse Grid Details: Fine Grid Details: # of Test Points:

## Slide 14: Test Times
Test vendors to provide approximate test times in RAN4#89 once an estimate of the dwell time is provided (considering the dwell time could have a significant impact on overall test time)