## Slide 1: Way Forward on TCI State Switching Delay
Intel Corporation
3GPP TSG-RAN WG4 Meeting #90 R4-1900112
Athens, GR, 25th Feb – 1st March, 2019

## Slide 2: Background
UE is configured TCI list via RRC for PDCCH and PDSCH
PDCCH active TCI state is configured via MAC CE
PDSCH can have up to 8 activated TCI states configured via MAC CE
PDSCH active TCI state is configured via DCI when applicable
If PDSCH active TCI state is not configured via DCI it follows TCI of PDCCH
DCI based TCI state/beam switch is applicable to PDSCH
MAC CE based TCI state/ beam switch is applicable to PDCCH

## Slide 3: DCI based TCI State Switch
The beam switching time for PDSCH activated via DCI is indicated by UE capability
Proposal #1: DCI based TCI state/ beam switch delay for PDSCH starts from the end of last symbol of PDCCH to beginning of the first symbol of PDSCH
Proposal #2: The delay for DCI based beam/ TCI state switch for PDSCH is defined by UE capability timeDurationForQCL

## Slide 4: MAC CE based TCI State Switch
2 possible cases for MAC CE based TCI state switch for PDCCH
  TCI state switch to a known TCI state
  TCI state switch to an unknown TCI state
Proposal #3: The delay for MAC CE based TCI state switch for PDCCH starts from the slot with PDSCH carrying the activation command to the slot when PDCCH can be received based on new TCI state
Proposal #4: The delay for MAC CE based TCI switch for PDCCH to a known TCI state is defined as TTCI-Switch, known = THARQ + 3ms.
Proposal #5: The delay for MAC CE based TCI switch for PDCCH to an unknown TCI state is defined as TTCI-Switch, unknown = TACQ-TO-FO + THARQ + 3ms