## Slide 1
3GPP TSG-RAN WG4 Meeting #90 R4-1900272
Athens, GR, 25th Feb – 1st March, 2019
Agenda Item: 6.12.9
WF on CSI-RS based RRM requirements
CMCC

## Slide 2: Agreements
Specify CSI-RS based RRM requirements in Rel-15 TEI.
Specify CSI-RS based RRM requirements for both measurement without MG and measurement with MG.
The scenario of measurement with MG and measurement without MG is identified as following:
  For the case of CSI-RS based RRM measurement without associated SSB, if CSI-RS is overlapped with active BWP, and target CSI-RS and serving CSI-RS have same SCS, UE perform CSI-RS based measurement without MG. If CSI-RS is non-overlapped with active BWP, MG is necessary. The details can be found in following Table1.
 | Target CSI-RS and serving CSI-RS have same SCS | Target CSI-RS and serving CSI-RS have different SCS
CSI-RS is overlapped with active BWP | MG is not needed | Whether MG is needed or not depends on UE capability
CSI-RS is non-overlapped with active BWP | MG is needed | MG is needed
Table 1 possible scenarios of CSI-RS based RRM measurement without accociatedSSB

## Slide 3: Agreements
  for the case of CSI-RS based RRM measurement with associated SSB, either PSS/SSS detection or CSI-RS measurement is performed with MG, it can be classified as measurement with MG. If both PSS/SSS detection and CSI-RS measurement are performed without MG, it can be classified as measurement without MG. The details can be found in following Table2.
 | Target CSI-RS and serving CSI-RS have same SCS |  |  | Target CSI-RS and serving CSI-RS have different SCS |  | 
 | Accociated SSB is intra-f w /o MG | Accociated SSB is intra-f w/ MG | Accociated SSB is inter-f | Accociated SSB is intra-f w/o MG | Accociated SSB is intra-f w/ MG | Accociated SSB is inter-f
CSI-RS is overlapped with active BWP | MG is not needed | MG is needed | MG is needed | Whether MG is needed or not depends on UE capability | MG is needed | MG is needed
CSI-RS is non-overlapped with active BWP | MG is needed | MG is needed | MG is needed | MG is needed | MG is needed | MG is needed
Table 2 possible scenarios of CSI-RS based RRM measurement with accociatedSSB

## Slide 4: Agreements
  for the case that target CSI-RS resource is covered by active BWP but has different SCS with serving CSI-RS resource, if UE supports simultaneousRxDataSSB-DiffNumerology or supportedSubCarrierSpacingDL, measurement gap is not needed. For the UE which do not support simultaneousRxDataSSB-DiffNumerology and supportedSubCarrierSpacingDL, measurement gap is necessary.
Reuse the measurement accuracy of SSB-based RRM measurement to specify the measurement accuracy of CSI-RS based RRM measurement.
Specify the CSI-RS measurement delay requirements for RRM as following.
Bandwidth | CSI-RS measurement delay for RRM
24 PRB | 10 samples
48 PRB | 5 samples
>=96 PRB | 3 samples