## Slide 1: Way Forward on CQI Reporting Requirements with 1024QAM
Intel Corporation
3GPP TSG-RAN WG4 Meeting #90 R4-1900453
Athens, GR, 25th Feb – 1st March, 2019

## Slide 2: Background
In RAN4#89 CQI test point SNR was agreed: 28/29 dB
Test point introduced at high SNR to target 1024QAM range
With new CQI table for 1024QAM entries have been modified
  CQI Index range 4 – 6 have discontinuities compared to 256QAM table
Need to introduce low SNR test point
  Target CQI Index 4,5
  Median CQI of 4 reported for SNR range 3-5 dB
  Median CQI of 5 reported for SNR range 6-9 dB

## Slide 3: Way Forward
Proposal : Introduce additional SNR test point of 4/5 dB or 6/7 dB for 1024QAM CQI reporting
Companies are encouraged to bring results in order to define CQI test at lower SNR point