## Slide 1: WF on FR2 OBW
Qualcomm
R4-1902147
3GPP TSG RAN4 #90
Athens, GR, 25 Feb-1 Mar 2019

## Slide 2: Background
The OBW requirement in TS38.101-2 is based on 99% power occupancy definition
R4-1900675 proposals to allow compliance with OBW requirement in FR2 UEs are below:
  Proposal 1: For PC2/3/4, the current definition of special 0dB MPR waveforms shall be removed. Instead some subset of inner waveforms shall be assigned 0dB MPR
  Proposal 2: For PC1, the current definition of special 0dB MPR waveforms shall be removed. Instead some subset of inner waveforms shall be assigned 0dB MPR
Agreement captured during online discussion of R4-1900675 in RAN4#90 is below:
  WF: we adopt proposal but the more detailed condition and proposed values need to be discussed during this meeting.

## Slide 3: Proposed Changes for PC1
MPR Table – Change to Inner columns
Modulation | MPRWT (dB) |  | 
 | Outer RB allocations, 50M, 100M, 200M, 400M | Inner RB allocations, ≤ 200M | Inner RB allocations, 400 M
DFT-s-OFDM PI/2 BPSK | ≤ [5.5] | ≤ [2.5] | ≤ 3.0
DFT-s-OFDM QPSK | ≤ [6.5] | ≤ [3.0] | ≤ 3.5
DFT-s-OFDM 16 QAM | ≤ [6.5] | ≤ [4.0] | ≤ 4.5
DFT-s-OFDM 64 QAM | ≤ [6.5] | ≤ [4.5] | ≤ 6.5
CP-OFDM QPSK | ≤ [6.5] | ≤ [4.5] | ≤ 5.0
CP-OFDM 16 QAM | ≤ [6.5] | ≤ [5.5] | ≤ 6.5
CP-OFDM 64 QAM | ≤ [7.5] | ≤ [7.5] | ≤ 9
Modulation | MPRWT (dB) |  |  |  | 
 | (Outer, all CBW) | Inner RB allocations, ≤ 200M |  | Inner RB allocations, 400M | 
 |  | RBstart ≥ Ceil(1/3 NRB) AND RBend ≤ Ceil(2/3 NRB) | RBstart < Ceil(1/3 NRB) OR RBend > Ceil(2/3 NRB) | RBstart ≥ Ceil(1/3 NRB) AND RBend ≤ Ceil(2/3 NRB) | RBstart < Ceil(1/3 NRB) OR RBend > Ceil(2/3 NRB)
DFT-s-OFDM PI/2 BPSK | (Unchanged) | 0.0 | ≤ [2.5] | 0.0 | ≤ 3.0
DFT-s-OFDM QPSK |  | 0.0 | ≤ [3.0] | 0.0 | ≤ 3.5
DFT-s-OFDM 16 QAM |  | ≤ [4.0] |  | ≤ 4.5 | 
DFT-s-OFDM 64 QAM |  | ≤ [4.5] |  | ≤ 6.5 | 
CP-OFDM QPSK |  | ≤ [4.5] |  | ≤ 5.0 | 
CP-OFDM 16 QAM |  | ≤ [5.5] |  | ≤ 6.5 | 
CP-OFDM 64 QAM |  | ≤ [7.5] |  | ≤ 9 | 

## Slide 4: Proposed Changes for PC2/3/4
MPR Table
 |  | Channel Bandwidth / MPRWT | 
 |  | 50 / 100 / 200 MHz | 400 MHz
DFT-s-OFDM | Pi/2 BPSK | 1.5 | 3.0
 | QPSK | 1.5 | 3.0
 | 16QAM | 3 | 4.5
 | 64QAM | 5 | 6.5
CP-OFDM | QPSK | 3.5 | 5.0
 | 16QAM | 5 | 6.5
 | 64QAM | 7.5 | 9.0
 |  | Channel Bandwidth / MPRWT |  |  | 
 |  | 50 / 100 / 200 MHz |  | 400 MHz | 
 |  | RBstart ≥ Ceil(1/3 NRB) AND RBend ≤ Ceil(2/3 NRB) | RBstart < Ceil(1/3 NRB) OR RBend > Ceil(2/3 NRB) | RBstart ≥ Ceil(1/3 NRB) AND RBend ≤ Ceil(2/3 NRB) | RBstart < Ceil(1/3 NRB) OR RBend > Ceil(2/3 NRB)
DFT-s-OFDM | Pi/2 BPSK | 0.0 | 1.5 | 0.0 | 3.0
 | QPSK | 0.0 | 1.5 | 0.0 | 3.0
 | 16QAM | 3 |  | 4.5 | 
 | 64QAM | 5 |  | 6.5 | 
CP-OFDM | QPSK | 3.5 |  | 5.0 | 
 | 16QAM | 5 |  | 6.5 | 
 | 64QAM | 7.5 |  | 9.0 | 

## Slide 5: Proposed Changes, Other
Identification of existing 0dB waveform in text of section 6.2 of TS38101-2 shall be removed. For example :
For each power class, a new reference waveform shall be selected from identified 0dB waveforms
The waveform defined by BW = 100 MHz, SCS = 60 kHz, DFT-S-OFDM QPSK, 128RB0 is the reference waveform with 0 dB MPR and is used for the power class definition.
UE requirements for the waveform defined by BW = 100 MHz, SCS = 60 kHz, DFT-S-OFDM pi/2 BPSK, 128RB0 shall be set to 0 dB MPR.
The waveform defined by BW = 100 MHz, SCS = 60 KHz, DFT-S-OFDM QPSK, 128RB0 is the reference waveform with 0 dB MPR and is used for the power class definition.

## Slide 6: Update of NW simulation assumptions
The new 0dB MPR waveform shall be assumed for network simulations related to outage and mean throughput evaluations
Update the NW simulation assumptions in TR38.817-01 as follows:
Scenario (in TR38.803) | Indoor hotspots | Dense Urban | Urban Macro
UE Elevation distribution | Uniform from 0 to 180 degree. |  | 
Indoor ratio | 100% | 0%(baseline), 20%, 100% | 
Resource Allocation (UL) (1) | ・15MHz for outage evaluation ・200MHz for mean throughout evaluation |  | 
Blockage Modeling | No body blockage and hand grip modelling |  | 
Target UL SNR | 22dB |  | 
Antenna pattern Modeling | Option1: Based on mathematical modelling Option2: Based on measured simulated pattern |  | 
Note 1: MPR may apply, or a resource allocation to align with the 0 dB MPR reference waveform may be used |  |  | 
Table 7.2.1.4.3-1: Network simulation assumptions

## Slide 7: Update of UL-RMC
UL-RMCs shall be updated to reflect new definition of 0dB waveform(s).