## Slide 1: WF on simulation assumptions for BC tolerance requirements
LG Electronics
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019
Agenda Item: 6.7.8.3.2
Document for : Approval
R4-1902254

## Slide 2: Background
RAN Plenary agreed to specify BC tolerance requirements for UE feature 2-20 set to 0 [1]
RAN4 agreed to decide [x]-tile % and [Y] dB based on delta EIRP CDF curve
  Candidate [x]-tile % is one of set in [80%, 85%, 90%, 95%, 100%]. In addition, companies can also check other point, e.g., 60%
Agreements in AH meeting [2]
  Test point is top 50% EIRP2 points for PC3 UE
  Option3 in Test procedure [2] is baseline
  Basic principle : Test procedure and test point will be decided as package to reduce the OTA test time [3]
  The same polarization combining option will be used for both EIRP1 and EIRP2[2]
    Option 3: EIRP CDF is derived based on data vector [maximum (V-V + V-H, H-V+H-H)] cross all testing points

## Slide 3: WF on General UE RF parameters
Basic RF parameters: reuse the simulation assumptions for Peak/Spherical EIRP requirements
UE RF parameters | Unit | Value | Notes
Frequency range |  | n257/n258/n260/n261 | Antenna performance can be different
Measurement Grid | degree | 7.5 or 15 | Peak EIRP is 7.5 Spherical EIRP is 15
# of element antenna in an antenna module/set (# of panels, # of operating beam, etc.) |  | 4 (2 panels, # total beam: 8,16,32) | Consider switched 2 panels. These parameters will be depend on UE implementation. Other values are not precluded
Polarization |  | 2 polarization | 
Constant density/step test grid for EIRP | Y/N | Y | Finite test point shall be the baseline
Beam phase shifter controller | degree | 45 | Finite beam shall be the baseline
Antenna location (front, back, top-side, left-side, right-side, bottom-side) |  | Left/right | combination of the lists are not precluded.
Phase shifter/Amplitude by pre-coder | Degree/ dB | Phase error =[5~45] deg Amplitude = [1~3]dB | These parameters will be depend on UE implementation. Other values are not precluded
Error in RSRP estimation | dB | =[2]dB | 
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | This information is meaningful only if it’s the same with the material which covers antennas.
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | 
Display panel – Full (Y) or Partial (N) | Y/N | Y | 
Bezel Margin | mm | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability

## Slide 4: WF on measurement method for delta EIRP
Simulation Set-up : option1
  1st : Select one EIRP measurement grid (with 7.5 or 15 degree) among all grids
    Measurement grid Point = Qn
  2nd : Get Delta_EIRP as following
    Define Autonomous Tx Beam direction (EIRP1)
      Peak Rx Beam(A1) = max{{RSRP_1+D1,RSRP_2+D2,…,RSRP_N+DN}_at high SNR
        D = RSRP_accuracy(+/-[2])dB
      Autonomous Tx Beam(A2) = A1 + phased shift/amplitude error
      EIRP1 = A2 at Qn
    UL Beam Sweeping Tx Beam direction (EIRP2)
      EIRP2 = max{EIRP_1, EIRP_2, …, EIRP_M} at Qn, m=1~M
        M = # of SRS resource(M=[4],…)
    Delta_ERIP = EIRP2-EIRP1
  3rd : iterated 1st ~2nd with next EIRP measurement grid, Qn+1
  4th : If all measurement grid points are run, get CDF of delta_EIRP

## Slide 5: WF on measurement method for delta EIRP
Simulation Set-up : option2
  Set Ideal AWT(Analog Beam Weight Table) for K beams ( depend on UE implementations)
    AWT = [V1 V2 V3 … VK];
  For each M UEs ( M is number of UE to be simulated)
    Generate Tx/Rx AWT considering Phase/Amplitude error (eT/eR = Phase/Amplitude error term at Tx/Rx)
      Tx AWT = [V1+eT1 V2+eT2 V3+eT3 … VK+eTK] = [VT1 VT2 VT3 … VTK]
      Rx AWT = [V1+eR1 V2+eR2 V3+eR3 … VK+eRK] = [VR1 VR2 VR3 … VRK]
    For Given Measure point(Q) within EIRP measurement grid
      Iterate until get statistically meaningful measurement values
        Decide UE Autonomous DL(Rx) Beam selection (EIRP1)
          Beam Index(k) = index of max(RSRP1+D1, RSRP2+D2, RSRP3+D3, … , RSRPK+DK) = index of max(G(Q, VR1)+D1, G(Q, VR2)+D2, G(Q, VR3)+D3, …, G(Q, VRK)+DK)
        EIRP1 = G(Q, VTk)
        EIRP2 = max(G(Q, VT1), G(Q, VT2), G(Q, VT3), …, G(Q, VTK)) (Beam sweeping and Select best)
        Delta_EIRP = EIRP2 – EIRP1
  If all measurement grid points are run, get CDF of delta_EIRP
DK= measurement error of RSRPK
G(Q, Vk) = Antenna Gain at Q direction with Vk beam vector)

## Slide 6: WF on SRS parameters
RAN1 common understanding for UL beam sweeping operation
  If UE does not configure the spatialRelationInfo from NW, then the UE can consider the UL beam sweeping.
  If UE has configure the spatialRelationInfo from NW, then the UE consider autonomous beam selection
    spatialRelationInfo contain the ID of a reference ‘ssb-Index’ or ‘csi-Rs-Index’ for SRS resource
Upper limitation of SRS-Resource
  To reduce the test time the upper number of SRS-Resource is [4] or [8] or [16] from TE
  <UplinkBeamManagement in TS38.331 v15.4.0>

## Slide 7: Reference
[1] RP-182879, “WF on Beam Correspondence,” Samsung
[2] R4-19002256, “Ad-Hoc Meeting Minutes for Beam Correspondence,” Samsung
[3] R4-1900xxxx, “Draft chairman meeting report for RAN4 #90,”
[4] R4-1900134, "on beam correspondence requirements," Intel Corporation
[5] R4-1900251, "Beam correspondence for tolerance based requirement with UE beam sweeping ," LG Electronics France
[6] R4-1900672, "FR2 Beam Correspondence, On Alternative Definition," Qualcomm Incorporated
[7] R4-1901278, "Beam Correspondence," Nokia, Nokia Shanghai Bell
[8] R4-1901315, "Beam Correspondence, remaining X and Y," Sony, Ericsson
[9] R4-1900431, “Verification of beam correspondence during initial access,” Ericsson, Sony
[10] R4-1900278, “On uplink beam sweeping based EIRP test procedure,” Ericsson, Sony
[11] R1-1900133, “On beam correspondence test procedure,” Intel Corporation
[12] R4-1900715, "Initial discussion on test procedure for beam correspondence in FR2," LG Electronics