## Slide 1: WF for NR PUSCH demodulation
R4-1902434
Document for: Approval
3GPP TSG-RAN WG4 RAN#90
Athens, Greece, 25th Feb – 1st Mar, 2019
Agenda: 6.14.2.2
Nokia, Nokia Shanghai Bell, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89

## Slide 3: PUSCH Test Applicability Rules
General agreements about handling of applicability rules in this meeting can be found in separate WF:
  WF on supported feature parameterization declaration for performance requirements (R4-1902071)

## Slide 4: PUSCH cases with only front-load DMRS cannot achieve 70% of max TP or max TP
Only remove cases that cannot achieve 70% max TP if [2] or more companies observed this issue.
Cases that can achieve 70% max TP but cannot achieve max TP.
  Option 1: Further check and discuss.
  Option 2: Further check and discuss, if [1] or more companies observe this issue.

## Slide 5: FR1: PUSCH resource mapping type B
The performance requirements for Type B should be defined as well in FR1 besides the requirements agreed to define for Type A
The same number of test cases should be introduced for Type B as those agreed cases defined for type A
The performance requirements for Type B FR1 shall be for slot based symbol allocation.

## Slide 6: PUSCH Test Applicability – TDRA types
Type A and Type B
  If BS supports both Type A and Type B, select the PUSCH requirements for Type A or Type B for test, otherwise BS vendor tests the PUSCH requirements for the declared Type A or Type B supporting.

## Slide 7: DMRS Configuration
PUSCH FR1
  Keep original agreements (both DMRS 1+0 and 1+1)
PUSCH FR2 with DMRS 1+1:
  For FR2 requirements with DMRS 1+1, company agreed to introduce the requirements, but need to down prioritize it. Down prioritization means the requirements for DMRS 1+1 can be introduced in Release 15 WI (completed by June, 2019) or in TEI-15by December,2019

## Slide 8: PUSCH Test Applicability – DMRS Configuration
DMRS configuration 1+0 and 1+1
  If BS supports both DMRS configuration 1+0 and 1+1, select the PUSCH requirements for DMRS configuration 1+1 for test, otherwise BS vendor tests the PUSCH requirements for the declared DMRS configuration 1+0 or configuration 1+1 supporting.

## Slide 9: PTRS configuration
For FR2 requirements with QPSK including cases for both CP-OFDM and DFT-s-OFDM, PT-RS is not configured, but RAN4 needs to rerun the related simulations.
For FR2 PUSCH requirements without PT-RS additionally configured for 16QAM and 64QAM, company agreed to introduce the requirements, but need to down prioritize it. down prioritization means the FR2 PUSCH requirements without PT-RS additionally configured for 16QAM and 64QAM can be introduced in Release 15 WI (completed by June, 2019) or in TEI-15 by December,2019.

## Slide 10: PUSCH Test Applicability – PTRS Configuration
If BS supports both with PT-RS configured and without PT-RS configured, select one of the PUSCH requirements for with PT-RS configured or without PT-RS configured for test, otherwise BS vendor tests the PUSCH requirements for the declared PT-RS configuration supporting.

## Slide 11: UCI on PUSCH
Discussed in a separate WF provided by Samsung.

## Slide 12: Scope of Rel-15 NR BS Demod PUSCH
The following features are not part of the Rel-15 scope
  PUSCH with 256QAM in FR1
  PUSCH with UL timing adjustment (non-HST cases).
  PUSCH requirements with 30% throughput metric in Rel-15 NR
  PUSCH requirements with 1 RB allocation in Rel-15 NR
  Based on agreement:
  No new BS demodulation requirement, which was not discussed in the previous meetings, should be introduced in Rel-15.
The question, if the HST feature (and corresponding subfeatures) are part of the scope of Rel-15, is discussed in separate WF.

## Slide 13: Test Parameters, CP-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1, 2
Number of Rx | 2, 4, 8 | 2
Number of layers | 1, 2 | 1, 2
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1, 1+1 (low prio)
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A and B | type B
Frequency domain resource | Full applicable test bandwidth | Full applicable test bandwidth
MCS index | 2, 16, 20 (20 only for 1Tx) | 2, 16, 20 (20 only for 1Tx)
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5MHz, 10MHz, 20MHz; 30kHz: 10MHz, 20MHz, 40MHz, 100MHz 60kHz(FR2): 50MHz, 100MHz; 120kHz: 50MHz, 100MHz, 200MHz | 
PTRS | Not configured | QPSK: Not configured 16 and 64 QAM: (Configured with KPTRS =2, LPTRS =1) and (not configured, low prio)
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 14: Test Parameters, DFT-s-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2, 4, 8 | 2
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | 1+1, 1 | 1, 1+1 (low prio)
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A and B | type B
Frequency domain resource | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW) | 60kHz: 30 PRB; 120kHz: 30 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5 MHz; 30kHz: 10 MHz | 60kHz: 50; 120kHz: 50
PTRS | Not configured | QPSK: Not configured
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput