## Slide 1: WF on Multi-slot PUCCH
R4-1902441
Document for: Approval
3GPP TSG-RAN WG4 RAN#90
Athens, Greece, 25th Feb – 1st Mar, 2019
Agenda: 6.14.2.1
ZTE, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808025, WF on NR PUCCH demodulation requirements in Rel-15, RAN4#87
  R4-1809556, WF on NR PUCCH demodulation performance requirements, RAN4#AH1807
  R4-1811727, WF on NR PUCCH demodulation performance, RAN4#88
  R4-1813943, WF on NR PUCCH demodulation requirements, RAN4#88bis
  R4-1816348, WF on NR PUCCH demodulation requirements, RAN4#89

## Slide 3: Background (Cont’d)
Agreements in the previous meetings:
Introduce requirements for multi-slot PUCCH for FR1 in Rel-15 by next June
  Option 1: Introduce requirements for PUCCH Formats 1 and 3 with slot repetition N = 2 and 4
    Define requirements by adding –10log(N)+[X] dB to single-slot PUCCH requirements, where X accounts for loss due to channel estimation and other errors.
      X:
        option 1 : X=1
        other options not precluded.
  Othe options not precluded.
Discuss the test parameters after the Nov meeting

## Slide 4: PUCCH format
PUCCH format
  Option 1: PUCCH format 3
  Option 2: PUCCH format 1
Notes: According to TS 38.213 Section 9.2.6, a UE can be configured a number of slots for repetitions of a PUCCH with format {1,3,4}

## Slide 5: Number of slot repetition N
Number of slot repetition N = 2

## Slide 6: Frequency hopping
Frequency hopping
  Option 1: Inter-slot frequency hopping enabled and intra-slot frequency hopping disabled
  Option 2: both intra and inter slot frequency hopping are disabled
Notes: If inter-slot frequency hopping enable, intra-slot frequency hoping must be disabled according to TS 38.213, or if inter-slot frequency hoping is disabled, intra-slot frequency hopping can be either enabled or disabled.

## Slide 7: Test Applicability
Test applicability for multi-slot PUCCH
Agreement
The requirements defined for multi-slot PUCCH only apply to the BS supporting multi-slot PUCCH.