## Slide 1: WF on LTE/NR spectrum sharing in Band 41/n41
KDDI, CMCC, Sprint
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019
R4-1902450

## Slide 2: Background
Two solutions are proposed for spectrum sharing in WID [1]
Solution#1: Create new NR band with requirements to achieve spectrum sharing (LTE and NR) in 2496 – 2690 MHz.
Solution#2: Addition of new requirements into n41 as below;
Introduce 100kHz channel raster support [RAN4]
Sync raster specification correction [RAN4]
Introduce UL 7.5kHz frequency shift [RAN4]
* above three requirements are at maximum for RAN4. If unnecessary, some of requirements may not be added into n41.

## Slide 3: Summary of discussion at RAN4#90
Solution#1 or solution#2?
  Support Solution#1: Qualcomm
  Support Solution#2: Sprint, CMCC, Ericsson, KDDI
Non-backwards compatibility issue of Rel-15 n41 UE without UL 7.5kHz frequency shift mentioned in [2] and [5] is the key issue to choose solution#2.
  UEs based on December version of the specifications could transmit UL without the UL shift as they were not required to support this shift
  (note: Applying UL 7.5kHz frequency shift to Rel-15 n41 UE [8] was
  not approved in RAN4#89.)

## Slide 4: Way forward (1/2)
To solve the compatibility issue of sulotion#2, verify feasibility of the following alternative plans
  Alternative#1: apply the following RRC information to n41 and clarify the UE behavior in Rel-15 to prevent UE without UL 7.5kHz frequency shift to access to spectrum sharing NW of n41
    One company declared that this proposal is a NBC (non backward compatibility change).
TS38.331
FrequencyInfoUL ::= SEQUENCE {
frequencyBandList MultiFrequencyBandListNR OPTIONAL, -- Cond FDD-OrSUL
absoluteFrequencyPointA ARFCN-ValueNR OPTIONAL, -- Cond FDD-OrSUL
scs-SpecificCarrierList SEQUENCE (SIZE (1..maxSCSs)) OF SCS-SpecificCarrier,
additionalSpectrumEmission AdditionalSpectrumEmission OPTIONAL, -- Need S
p-Max P-Max OPTIONAL, -- Need S
frequencyShift7p5khz ENUMERATED {true} OPTIONAL, -- Cond FDD-OrSUL-Optional
...
}
FrequencyInfoUL field descriptions
frequencyShift7p5khz
Enable the NR UL transmission with a 7.5KHz shift to the LTE raster. If the field is absent, the frequency shift is disabled.

## Slide 5: Way forward (2/2)
To solve the compatibility issue of sulotion#2, verify feasibility of the following alternative plans
  Alternative#2: deploy SSB of spectrum sharing NW where Rel-15 UE cannot find it. For spectrum sharing, we need to enable repetition of sync raster (M=1,3,5) in Rel-16 which has more sync raster entries compared to Rel-15.
    Feasibility of this proposal needs to be further verified and it will make constrains on operator’s NW deployment.
  Alternative#3: other solutions are not precluded.
Other aspects need further discussion
  For Scell management and handover purposes, the Rel-16 UE needs to inform the capability of supporting the 100kHz raster to the network.
    Need new capability in Rel-16 if use n41: Nokia, Qualcomm
    Not need new capability in Rel-16: Huawei, Samsung, CMCC

## Slide 6: Reference
[1] RP-182883, “New WI proposal: LTE/NR spectrum sharing in Band 41/n41,” KDDI Corporation
[2] R4-1900654, Discussion on LTE/NR spectrum sharing in Band 41/n41, Huawei, HiSilicon
[3] R4-1900312, Overview on LTE/NR spectrum sharing in Band 41/n41, Samsung
[4] R4-1900437, 100 kHz raster for Band n41, Ericsson
[5] R4-1900571, Way forward on LTE/NR spectrum sharing in Band 41/n41, KDDI Corporation
[6] R4-1900589, Discussion on LTE/NR spectrum sharing in Band 41/n41, Nokia, Nokia Shanghai Bell
[7] R4-1901853, 100 kHz raster for n41, Sprint Corporation
[8] R4-1814707, Support of 7.5 kHz carrier shift for additional operating bands, Ericsson, KDDI