## Slide 1: WF on co-existence study of CLI
LGE, Ericsson, Huawei, Nokia, Qualcomm
3GPP TSG-RAN WG4 Meeting RAN4#90 R4-1902506
Athens, Greece, 25th Feb. – 1st March, 2019
Agenda: 8.2.1
Document for Approval

## Slide 2: Background
Based on the WID, RAN4 needs to perform coexistence study to identify conditions of coexistence among different operators in adjacent channels.
  Target no or very minimal impact on RF requirement
In RAN4 #90 meeting, the work plan of CLI and RIM (R4-1900222) was approved.
  Proposal: Approve the proposed work plan for CLI to complete Core and Performance requirements in time.

## Slide 3: Proposal
Companies are encouraged to provide co-existence simulation results based on agreed simulation scenarios and parameters
  Co-existence study of BS-to-BS and UE-to-UE
  Evaluation metric
    T-put
      Without dynamic TDD (for baseline) and with dynamic TDD
      ccdf’s at 50%-tile and 5 %-tile figures
    SINR statistic
  Traffic mode
    Low (RU = 10%) and full buffer
Simulation assumptions can be found in R4-1902507

## Slide 4: Proposal
Scenario No. | Deployment Scenario (Aggressor->Victim) | Simulation frequency | Aggressor baseline | Aggressor in CLI | Victim
1 | Macro -> Macro | 4 GHz | NR, 100 MHz, DL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, UL 100% | NR, 100MHz, DL
2 |  |  | NR, 100MHz, UL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, DL 100% | NR, 100MHz, UL
3 |  | 30 GHz | NR, 200MHz, DL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, UL 100% | NR, 200MHz, DL
4 |  |  | NR, 200MHz, UL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 200MHz, UL
5 | Micro -> Micro | 30 GHz | NR, 200MHz, DL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 200MHz, DL
6 |  |  | NR, 200MHz, UL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 200MHz, UL
7 | Macro -> Indoor | 4 GHz | NR, 100MHz, DL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, UL 100% | NR, 100MHz, DL
8 |  |  | NR, 100MHz, UL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, DL 100% | NR, 100MHz, UL
9 | Indoor -> Macro | 4 GHz | NR, 100MHz, DL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, UL 100% | NR, 100MHz, DL
10 |  |  | NR, 100MHz, UL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, DL 100% | NR, 100MHz, UL
11 |  | 30 GHz | NR, 200MHz, DL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 200MHz, DL
12 |  |  | NR, 200MHz, UL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 200MHz, UL
13 | Indoor -> Indoor | 4 GHz | NR, 100MHz, DL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, UL 100% | NR, 100MHz, DL
14 |  |  | NR, 100MHz, UL | NR, 100MHz, DL 50%+UL 50% NR, 100MHz, UL 100% | NR, 100MHz, UL
15 |  | 30 GHz | NR, 200MHz, DL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 100MHz, DL
16 |  |  | NR, 200MHz, UL | NR, 200MHz, DL 50%+UL 50% NR, 200MHz, DL 100% | NR, 100MHz, UL
Scenarios for simulation
Aggressor: Dynamic TDD