## Slide 1: WF on NR V2X UE RF parameters and transient period
LG Electronics
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019
Agenda Item: 10.5
R4-1902511

## Slide 2: Background [1]
AGC setting time [1][7]
Enhanced IBE model [2]
Transient period [3][4][5][6][7][10]
In previous RAN4 meeting, general UE RF parameters were replied to RAN WG1 for AGC setting time and IBE model as follow [6]
  AGC settling time
    At least AGC settling time = 1 OFDM symbol for 15 kHz SCS is feasible.
    RAN4 will further study if smaller AGC time is achievable incl. 15 kHz SCS.
  IBE model
    Model 1: {W, X1, X2, Y1, Y2, Z1, Z2, Z3 and Z4} = {3, 6, 3, 3, 3, 3, 3, 3, 3} (note: this model is using same approach as in TR 36.843)
    Note that other models are under discussion in RAN4 and may be provided at a later stage.

## Slide 3: Background [2]
RAN1 send LS [9] to RAN4 for the clarification on transient period
  Illustration of the candidate sidelink PSCCH/PSSCH configuration options:
  RAN1 working assumptions
    Regarding PSCCH / PSSCH multiplexing, at least option 3 is supported for CP-OFDM.
      RAN1 assumes that transient period is not needed between symbols containing PSCCH and symbols not containing PSCCH in the supported design of option 3.
      FFS how to determine the starting symbol of PSCCH and the associated PSSCH
      FFS for other options. e.g. whether some of them are supported to increase PSCCH coverage.

## Slide 4: WF on AGC settling time
AGC settling time includes the following components (AGC setting time =a+b+c+d)
  (a) time offset from the start of the OFDM symbol to account for maximum signal propagation delay from different UEs
  (b) time to receive the window of samples used for estimating the gain
  (c) time for estimating and programming the desired gain setting
  (d) time for the gain setting taking into effect
Open issues :
  FFS if same or different AGC settling time shall be applied for different SCS
  AGC settling time will be derived under assumption of minimum V2X resource allocation RB size restrictions. RBs size restrictions are FFS:
    Option1
      At least 10RBs for 15kHz
      At least 5 RBs for 30kHz
      At least 3 RBs for 60kHz
    Option2
      At least 10RBs for all SCSs
Further study feasible AGC settling time for FR1
  Companies are encouraged to bring analysis on
    AGC accuracy and RX power estimation duration depending on the CBW, V2X signal RB size, SCS
    AGC settling time duration dependency on the number of V2X CCs and RX chains
  Aim to send LS with final AGC settling time value to RAN1 in RAN4 #90bis

## Slide 5: WF on enhanced IBE model
RAN4 will further discuss on the enhanced IBE model for NR V2X UE.
Interested companies are encouraged to provide the preferred IBE model for NR V2X UE at next RAN4 meeting.
Based on the analyzed results, RAN4 can send LS to inform the IBE model at FR1.

## Slide 6: WF on transient period
Questions : RAN1 would like to ask the following questions for options 1A, 1B, and 3 when the total transmit power does not change between the last symbol containing PSCCH and the following symbol:
  Q1: Whether transient period is needed (if so, how much) if power spectral density is different between the last symbol containing PSCCH and the following symbol
  A1: Yes, in case of RB configuration or total transmit power change, transient period is needed, which could result in phase discontinuity for PSSCH.
    Basically, RAN4 define transient period as shown in section 6.3.3 in TS38.101-1
    between transmit OFF power and transmit ON power symbols (transmit ON/OFF)
    between continuous ON-power transmissions with power change or RB hopping is applied.

## Slide 7: WF on transient period
Q2: Whether transient period is needed (if so, how much) if PSCCH and PSSCH use different frequency location and/or resource size in option 1B and 3
A2:
  Option 1B could result in a different RB configuration (location and/or Size), power spectral density for control than that for data. This could result in a different MPR and AMPR for control and data. Hence, this option needs a transient period.
  Option 3: This option will not need any transient period. In RAN4, MPR and AMPR should be derived for the entire slot and a single value of MPR/AMPR should be used for the entire slot.

## Slide 8: WF on transient period
Q3: Whether there is any impact on the above questions due to different assumptions of amplifiers (e.g., for MIMO purpose, etc.)
A3:
  In the case where PSCCH is rank-1 and transmitted from one antenna only, while PSSCH is transmitted from both antennas, the transient period will be needed. It will result in phase discontinuity for PSSCH.
  In the case where PSCCH and PSSCH are transmitted from same the antennas connectors, the answers to the above questions are not impacted.

## Slide 9: WF on transient period
Q4: Whether there are any other cases that require transient period (if so, how much)
A4: RAN4 can provide additional analysis result once sidelink physical design becomes clearer.

## Slide 10: Reference
[1] R4-1900691, "On AGC settling time," MediaTek inc.
[2] R4-1900165, "On V2X IBE model," Intel Corporation
[3] R4-1900270, "Reply LS on NR UE transient period in sidelink channels," LG Electronics France
[4] R4-1900164, "Reply LS on transient period in sidelink channels," Intel Corporation
[5] R4-1901669, "Discussion of Reply LS for NR V2X," Ericsson
[6] R4-1900405, "On V2X transient periods for RAN1 LS reply,“ InterDigital
[7] R4-1901764, "Discussion on Transient Period and AGC Settling Time for NR V2X, “ Qualcomm
[8] R4-1816666, "Reply LS on NR V2X RF parameters for RAN1 physical layer design aspects"
[9] R4-1900005, "LS on transient period in sidelink channels," RAN1, LG Electronics
[10] R4-1900667, "LS reply on transient period in sidelink channels," Huawei
[11] R4-1900381, “Further discussion on NR V2X RRM characteristics,” Intel